1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

104 - Controls - Gunner - Joystick
U=Up, D=Down, F=Forward, B=Backward, L=Left, R=Right, P=Press, S-*=Shift-*, L-*=Long-*

Trigger
- P1: --
- P2: Release Weapons (everything but missiles)
Flip-down trigger
- P: Trimmer button (press to set trim position immediately)
- S-P: Trimmer reset
Red button
- P: Fire ATGM (fires missiles only)
- S-P (3x): --
Upper gray button
P: Center VR view
Lower gray button
P: Launch Countermeasures
Trim hat
- P: Toggle Petrovich AI menu
- U/D/L/R: Trim controls (when Petrovich menu is not active)
- U/D/L/R: Petrovich menu controls (when Petrovich menu is active)
Dish hat
- U: 9K113 Aiming Profile - ON/OFF (lean into sight toggle)
- D: 9K113 Aiming Station, Zoom x3/x10 Lever (toggle zoom)
- L: --
- R: --
- P: OBSERV. Switch toggle
- S-P: DIAFR. OPEN switch toggle (when OPEN/up, overrides ATGM shoot limits)
- S-U: Backlight switch toggle (turns on reticle illumination)
- S-L: Laser Filter toggle (toggles green laser filter)
- S-R: Orange Filter toggle (toggles orange contrast filter)
MANVR/PC hat -- Mouse and zoom
Index Finger Hat -- View and Game controls
- F: F6 Weapon view	S-F: Active pause
- B: F2 External view	S-B: Info bar view toggle
- U: F1 Cockpit view	S-U: Rearm/Refuel window
- D: F10 Map view	S-D: Show controls indicator
- P: Toggle show control stick	S-P: Toggle show pilot body
Gray Reset hat
- P: Trimmer button (press to set trim position immediately)
- S-P: Trimmer reset
- F: Turn to the Sight Direction (when Petrovich is pilot)
- B: 9K113 Aiming Station, Reset Emission (resets guidance transmitter for next missile)
- L/R: LNCHR Rotary Selector Prev/Next (selects prev/next station for ATGMs)
Brake lever
- Axis: -- (no wheel brakes in front seat)
- P: --