1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

303 - Flight - Aircraft Info, Performance Limits

Aircraft Info
- Fuel:
  - Internal: 3750 lbs/1701 kg
  - External fuel tanks: 970 lbs/440 kg fuel each (total weight 1213 lbs/550 kg each, empty weight 243 lbs/110 kg)
- Best climb speed: 130-140 kph

Performance limits
- Max fully loaded speed: ~310 kph (167 kts) (with 4x ATGM + 4x rocket pods or 8x ATGM + 2x rocket pods)
- Vne speed: 335 kph officially. Retreating blade stall happens ~370 kph, may roll uncontrollably to the right; flatten collective immediately to attempt recovery.
- Engine power limits:
  - Max Rated/Takeoff: 990 deg C TIT, 101% N1, 6 minutes
  - Max Limited Cruise: 955 deg C TIT, 99% N1, 60 minutes
  - No time limits below these, but higher temps and RPM may reduce engine service life.
- Main rotor RPM limits:
  - Max Rated/Takeoff: 103% RPM max, 20 sec; 88% RPM min, 30 sec
  - Max Limited Cruise: 101% RPM, 20 sec
  - Below Max Limited Cruise: 103% RPM, 20 sec
- Normal cruise rotor RPM: 93-97%
- Generator cutoff RPM: 86-88%