1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

401 - A/A - R-60M (AA-8 Aphid-B)

General notes
- Max range 8km?? Min range 200m.
- Limited all-aspect.
- 40 deg FOV (+/-20 off boresight).
- When missiles are carried, pilot's cockpit will have 2 extra panels:
  - A2A MSL panel, left front canopy rail -- Missile system power and missile selection.
  - Right side of gunsight, missile lock lights.
- R-60s can only be carried on center pylons (2 and 5).
- Single missile weighs slightly less than a pair of ATGMs, double missile weighs slightly more than a pair of ATGMs.
- Missile equipment and ability to carry them is enabled by default (checked) in the ME. If the box is unchecked, missiles are restricted in the weapon restriction settings. If box is re-checked, missiles must be manually un-restricted.
- Missiles are highly susceptible to flares.

Using R-60M (AA-8 Aphid-B)
1. A2A MSL panel (left front canopy rail):
  1. PWR switch ... ON
  2. AIR/GND switch ... AIR
  3. LNCHR selector knob ... 1 (left pylon) or 2 (right pylon) (3 and 4 are unused)
  - When A2A MSL panel is ON, Petrovich AI ATGM launch command button is disabled.
1. Weapon selector knob ... OFF/MSL (center console between legs) (Gray Reset Hat left)
2. Seekers take ~60 seconds to power on, SEEKR OPR light next to gunsight turns on when ready.
3. Put target in gunsight rings to lock. When you have tone (beeping), LOCK ON light next to gunsight will turn on.
4. Fire with Trigger.
5. Seeker will automatically uncage and continue tracking the target. If lock is lost, seeker will re-cage. There is no ability to manually cage/uncage.