1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A/G - Gunner - Petrovich AI

When in front seat:
Trim Hat press will open an HSI-like display in FLT mode:
FLT (Flight) mode:
Left Short	Change to CBTM mode
Right Short	Shows reticle for head-tracking steering. Second press orders new heading where you're looking.
Left Long/Right Long	Set desired heading left/right.
Up Long/Down Long	Set desired altitude up/down.
Up Short/Down Short	Set desired speed faster/slower, will go to HVR (Hover) mode if speed under 50 kph

CBTM (Combat Maneuvers) mode:
Left Short	Change to FLT or HVR mode depending on speed.
Right Short	--
Left Long/Right Long	--
Up Short	Turn to where ATGM scope is looking.
Up Long	Begin ATGM attack run. Petrovich will maneuver to firing parameters for ATGM (nose down to point reticle at target) and will hold that attitude until max speed is reached, then return to level flight.
Down Long	Perform 180 deg combat evasion turn. Turn off OBSERV switch (gyros) for faster turn.

HVR (Hover) mode:
Left Short	Change to HVRT mode
Right Short	Shows reticle for head-tracking steering. Second press orders new heading where you're looking.
Left Long/Right Long	Set desired heading
Up Long/Down Long	Set desired altitude
Up Short/Down Short	Set desired speed, will go to FLT mode if speed over 50 kph

HVRT (Hover Translate) mode:
Left Short	Change to HVR mode
Right Short	Shows reticle for head-tracking steering. Second press orders new heading where you're looking.
Left Long/Right Long	Translate left/right while held.
Up Long	Translate forward while held.
Down Long	Perform 180 deg combat evasion turn. Turn off OBSERV switch (gyros) for faster turn.
Up Short/Down Short	Set desired speed, will go to FLT mode if speed over 50 kph