1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

503 - A/G - 30 mm Cannon, Rockets

MG-30 (GSh-30K) -- fixed 30 mm cannon with 260 rounds
Select Weapon knob ... FXD MG-30 (Gray Reset Hat back) (center console)
  - "30" should light up below gunsight.
1. "MG BURST" Burst Length switch ... As desired (SHORT/LONG/MEDIUM) (center console)
2. "MG RATE" Cannon fire rate SLOW/FAST switch ... As desired (INCR/DECREASE, toggle with Shift-Gray Reset Hat back) (center console)
  - INCR (fast) is 2000-2600 rpm (~6 seconds total firing time??)
  - DECREASE (slow) is 300-400 rpm (~45 seconds total firing time??)
When in range, fire with Trigger.

Rockets
Note: Automatic gunsight CCIP pipper only works with S-5 and S-8 rockets, not with S-13 or S-24.
Select Weapon knob ... ROCKET (Gray Reset Hat right) (center console)
  - "RKT" should light up below gunsight.
"MG BURST" Burst Length switch ... As desired (SHORT/LONG/MEDIUM) (center console)
Rocket	Short	Medium	Long	Notes
S-8 80mm and S-5 57mm	4	8	16	Per pod
S-13 122mm	1	2	5 (entire pod)	Per pod
S-24 240mm	1 (single)	??	2 (pair)	Rockets fire in balanced pairs; if unsymmetrical, fires the single asymmetrical rocket, then prefers outer first, then inner

1. ROCKET SIDES switch ... As desired (LEFT/BOTH/RIGHT) (center console)
2. When in range, fire with Trigger. Rockets ripple in bursts up to the burst length switch setting while Trigger is held.