1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

202 - Ground - Preflight, Performance Limits

Before takeoff (hot start or auto started)
1. Arm weapons ... As needed, see steps on other checklist (much easier to do this on the ground than in the air)
2. Doppler navigation system ... As desired, also set heading bugs if needed.
3. Left and Right Pitot Heat switches ... As needed (panel above and right of copilot's head)
4. Left and Right Dust Protection switches ... As needed (panel above and right of copilot's head)
5. Engine de-icing systems ... As needed (see info on other page)
6. Radios ... As desired (see steps on other page)
7. Countermeasures system ... ON, set to BOTH (see info on other page) (copilot right knee)
8. Fuel Meter switch ... TOTAL (copilot instrument panel)
9. Lights ... As desired:
  1. Pilot and Copilot instrument lights: Large knobs above behind pilot and copilot heads.
  2. Engineer instrument lights: Large knobs on right side wall behind engineer.
  3. Doppler nav computer, radar alt, drift and hover indicator lights: 5.5V LIGHTS switch (copilot triangular panel) and 5.5V LIGHTS BRIGHTNESS rheostat turned up (behind copilot, reach from pilot or engineer seat)
  4. Rotor tip, navigation, formation, anti-collision, etc. lights: Switches above right of copilot.
10. Cockpit window ... Close
11. Cockpit fans ... On (switches on panels above and diagonally outboard of pilot and copilot)

Performance limits
- Fuel:
  - Internal: 4253 lbs/1929 kg
- Cruise and endurance speed up to 1000 m: 220-240 kph normal, 205-215 kph at MTOW, slower at higher altitudes
- Best climb speed: 120 kph to 2000 m, 100 kph at 4000 m or more
- Vne speed: ~370 kph, due to retreating blade stall
- Autorotate glide speed: 180-190 kph
- Engine modes and limits (PSS is Particle Separator System/dust protection):
Mode	Norm N1 / (at 35 ℃)	Max N1 / (at 35 ℃)	NR	Norm TIT / (PSS off / on)	Max TIT	Time
Max Rated	97.7 / 97.7 %	101.0 %	93±1 %	920 / 915 ℃	990 ℃	6 min
Take Off	96.6 / 96.6 %	101.0 %	93±1 %	890 / 885 ℃	990 ℃	6 min
Max Ltd. Cruise	95.0 / 95.5 %	99.0 %	95±2 %	845 / 855 ℃	955 ℃	60 min
Ltd. Cruise	93.9 / 94.4 %	97.5 %	95±2 %	815 / 825 ℃	910 ℃	Unlimited
Cruise	92.0 / 92.5 %	95.5 %	95±2 %	770 / 780 ℃	870 ℃	Unlimited

  - Table shows N1 at ambient temperature of 35 ℃ or more. If cooler, subtract 1.5% per 10 ℃.
  - See manual PDF page 49 for normal N1 values, page 237 for max N1 values, 240 for NR values.
- Main rotor RPM limits:
Mode	Norm	Time	Max	Time
Max Rated	94 %	6 min	103 %	10 sec
Take Off	94 %	6 min	103 %	10 sec
Max Ltd. Cruise	97 %	60 min	101 %	20 sec
Ltd. Cruise	97 %	60 min	103 %	20 sec
Cruise	97 %	Unlimited	103 %	20 sec

Generator cutoff RPM: 86-88%