1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A/G - All

All weapons
1. Circuit breaker switch groups 1, 2, and 3 ... ON (left-most column of switches, use gang bars for each group)
2. Master Arm (Safety Switch) ... ON (above, left, and behind pilot's head) (B2 button)
3. Main Switch (RS/GUV Selector Switch) ... ON (default) (left of circuit breaker group 2)
4. Gunsight depression ... Red triangle (for most weapons)

B8V20A Rocket pods -- standard 20-round rocket pods
1. Pod Variant dial ... I (default) (copilot right upper windshield box) (Gray Reset Hat left)
2. UPK/RS switch ... RS (default) (Gray Reset Hat back)
3. Fire Test Unit Arm button ... Press and hold until all lights corresponding to mounted pods light up in the lower row of lights (left of circuit breaker group 2)
4. Press trigger to fire.

UPK-23-250 23mm cannon pods -- twin-barrel 23 mm cannon
1. Pod Variant dial ... I (default) (copilot right upper windshield box) (Gray Reset Hat left)
2. UPK/RS switch ... UPK (Gray Reset Hat forward).
3. Press trigger to fire.

9A624/9A622 Gun pods (GUV YakB GSHP) -- 2x 7.62 mm miniguns + 1x 12.7 mm minigun per pod
1. Pod Variant dial ... GUN (copilot right upper windshield box) (Gray Reset Hat right)
2. Modes triangular switch ... 800 IN OR 624 for .50 cal miniguns, or 622 for .30 cal miniguns (bigger number = bigger caliber) (above pilot)
3. Press trigger to fire.

9A800 Grenade launcher pods (GUV AP-30) -- 30 mm automatic grenade launcher
1. Pod Variant dial ... GUN (copilot right upper windshield box) (Gray Reset Hat right)
2. To fire pods on outer pylons:
  1. Modes triangular switch ... IN 800 OUT (above pilot)
  2. guarded switch ... 624/622+800 (default)
3. To fire pods on middle pylons:
  1. Modes triangular switch ... 800 IN OR 624 (above pilot)
  2. guarded switch ... 800
4. To fire pods on outer and middle pylons simultaneously:
  1. Modes triangular switch ... IN 800 OUT (above pilot)
  2. guarded switch ... 800
5. Press trigger to fire.

Quick switching using Rockets and UPK cannon pods
- Set up rockets and cannon pods as shown above.
- Switch back and forth by setting UPK/RS switch to UPK (cannons) or RS (rockets).

Quick switching using Rockets and GUV YakB GSHP pods
- Set up rockets and gun pods as shown above.
- Switch back and forth by setting Pod Variant dial to I or GUN (B3 and B6 buttons).