1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

202 - Ground - Preflight, Performance Limits

Preflight checklist
1. Guns ... Arm (three buttons on left side of instrument panel, press and hold until lights on center console come on)
2. Gun safety ... Off (red lever on top of stick) (Flip Down Trigger press)
3. If using external tanks: Drop Tank Signal Switch ... ON (center console)
4. Begin taxi; Rooksie brakes.

Performance limits
- Fuel:
  - Internal: 2584 lbs/1172 kg/~1050 L
  - Drop tanks:
    - with 2x 300 L: 3682 lbs/1670 kg total fuel
    - with 2x 400 L: 4048 lbs/1836 kg total fuel
    - with 2x 600 L: 4780 lbs/2168 kg total fuel
- Max speed with external tanks:
  - Small tanks (2x 300 L): 0.9 Mach, 5 Gs
  - Large tanks (2x 600 L): 0.85 Mach
- Service ceiling: 15000 m without drop tanks, 13400 m with drop tanks
- Stall speed:
  - Idle power, flaps and gear extended: 190 kph
  - Idle power, flaps and gear retracted: 200 - 220 kph below 10000 m, 230 - 240 kph above 10000 m
  - Max power, flaps and gear retracted: 200 kph