1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

302 - Flight - Navigation, Jettison, Engine air start

Navigation to NDB (Non-Directional Beacon) -- WIP Needs verification
Find a beacon on the map, looks like a little sunburst with a frequency in kHz beside it and two letters.
  - If the map icon has little "ears" around it, the NDB doubles as an inner or outer marker for an airfield.
1. Tune the ARK-5 radio system to the frequency (right console):
  1. Set CW/VOICE switch to VOICE??
  2. Set mode knob to COMP (automatic mode).
  3. Set frequency band selector to the one covering the frequency of the NDB.
  4. Turn the tuning crank to the correct frequency. Watch the signal strength needle at the top.
  5. Listen for the correct Morse code of the two letters associated with the NDB (see kneeboard page 002 for Morse code).
2. Radio Compass instrument (upper right of instrument panel) shows relative bearing to NDB. When the needle is pointing straight up, you're flying directly at the NDB.

Jettison
When external fuel tanks light turns on: Emergency Bomb Release button ... Press (red guarded switch on center console)
  - Note: External fuel tanks light will be on when on the ground. If drop tanks are equipped, it'll turn off after takeoff and remain off until tanks are empty.
Drop Tank Signal Switch ... OFF (center console).

Engine air start
1. Must be between 6000 m and 2000 m altitude, 300 to 320 kph IAS.
2. Throttle at idle??
3. Air Start switch ... ON (left wall forward of throttle)
4. Another step here?? Open shut-off valve??
5. When RPM starts to increase, put throttle at idle.
  1. If engine doesn't start in a few seconds, smoothly and slowly move the throttle forward and backward (15 seconds for full throw each way).
6. Air Start switch ... OFF (left wall forward of throttle)
7. Resume normal flight.