1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201 - Ground - Cold Start

Cold Start -- Autostart cannot be customized, default start sequence takes 2m55s, manual startup below is much much faster
1. Right wall switches: Bottom row, all on except rear 2. Top row, all on except front 2 and rear 1.
2. Left wall switches: All on except rear 4.
3. Throttles to IDLE (Bottom Thumb Button and shift-Bottom Thumb Button, moves throttles out of STOP latches)
4. Engine start buttons, left and right ... Press and release both (black guarded switches on left wall behind throttle)
  - Engines should stabilize at 4100 to 4300 RPM, OIL warning light should go out and you're ready to taxi.
  - Continue with remaining steps in the meantime.
1. Oxygen diluter lever ... MIX (left console rear, behind Flaps control panel)
2. Canopy ... Close (locks and pressurizes automatically)
3. Radar power switch ... STANDBY (left wall middle, top, or Middle Finger Hat up once)
4. Wheel chocks ... Remove
5. When engine OIL warning lights (warning light panel to right of RPM gauge) go out, you're ready to taxi.

Follow remaining steps in preflight checklist on following page.