1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Takeoff, Navigation, Jettison, Landing

Takeoff -- WIP needs verification
1. Nosewheel brake lever ... On (horizontal) (upper left instrument panel, near bottom left corner of gunsight base)
2. Flaps ... Takeoff position (T6 down)
3. Brakes will hold 11,000 RPM (approx the front of the Virpil throttle detent).
4. Recommended to use Mil or AB for takeoff (full throttle, then Pinky switch down or up and hold until lights come on)
5. Rotate at 200 kph to get nosewheel off the ground.
6. Liftoff around 280 kph.
7. Gear up before 500 kph.
8. Flaps up before 800 kph.

Navigation to NDB (Non-Directional Beacon) -- WIP Needs verification
Find a beacon on the map, looks like a little sunburst with a frequency in kHz beside it and two letters.
  - If the map icon has little "ears" around it, the NDB doubles as an inner or outer marker for an airfield.
1. Set Radio Audio Selector switch to RADIO COMPASS (radio panel in front of throttle).
2. Set the NEAR/FAR homing switch to NEAR (upper left instrument panel).
3. Tune the ARK-5 radio system to the NEAR (inner) beacon frequency (right wall):
  1. Set TLG/TLF switch to TLF.
  2. Set mode knob to ANT.
  3. Set frequency band selector to the one covering the frequency of the NDB.
  4. Turn the tuning crank to the correct frequency. Watch the signal strength needle at the top.
    - NOTE Do not turn the tuning crank with mode knob set to COMP, that may damage the tuning motor.
  1. Listen for the correct Morse code of the two letters associated with the NDB (see kneeboard page 002 for Morse code).
  2. Set mode knob to COMP. Direction to Inner Beacon should show on the radio compass gauge.
2. Repeat steps above to tune to the FAR beacon frequency, starting by setting the NEAR/FAR switch to FAR.
3. Radio Compass instrument (upper right of instrument panel) shows heading to NDB.
4. When you fly directly over the beacon, the BEACON light (above right of airspeed gauge) will flash. Then change the NEAR/FAR switch to NEAR to track the inner beacon on landing approach.

Jettison
- Drop tanks are empty when EXT TANKS EMPTY light illuminates (center console between legs, upper right corner)
- Jettison with EMERG. JETT. BOMBS TANKS red guarded button on left forward canopy rail next to the gun arming buttons.

Landing -- WIP needs verification
1. Nose gear brake lever ... On (horizontal) for maximum braking (upper left instrument panel, near bottom left corner of gunsight base)
2. Use speedbrakes to slow down (they are out only while button is held down, and retract automatically when you let go)
3. Under 500 kph: Gear ... Down
4. Under 400 kph: Flaps ... Landing position (shift-T6 down)
5. Final turn speed is 380 kph.
6. Approach speed is 300-310 kph.
7. When crossing threshold, throttles to idle and flare for landing.
8. Normal landing speed is around 235 kph.
9. Flaps ... Retract (T6 up)
10. (optional) Under 300 kph: Deploy drag chute (shift-T5 down)
11. Under 210 kph: Use wheelbrakes to slow down. Rooskie brakes.
12. After stopping:
  1. Jettison drag chute (yellow guarded button on left front canopy rail)
  2. Nose gear brake lever ... Off (vertical) for taxi (upper left instrument panel, near bottom left corner of gunsight base)