1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

401 - A/A - Radar, Guns, Missiles

Fence In
1. Right wall switches: Bottom row, all on except rear 2. Top row, all on except front 2 and rear 1.
2. Left wall switches: All on except rear 4.
3. Left and Right Gun Arm buttons ... Press and hold for at least 2 seconds each (B4 and B5 buttons, or left front canopy rail) until red arming lights (center console between legs) are lit
4. ARM BOMBS FUSE switch ... ON (center console between legs, top left corner)

Radar
General info
- Max range: 12 km, Azimuth: +/-60 deg, Elevation: +26/-16 deg.
- Range, Azimuth, and Elevation cannot be changed.
- Targets shown with "⊥" are above you, "+" are co-altitude, "T" are below you
- Can be used for 15 minutes, then must be turned off for 1 minute to cool down.
- Has a High Altitude mode (>2000 m) and Low Altitude mode (<2000 m, disables search antenna).
- Locking range in Low Altitude mode is greatly reduced and radar "bird" pipper is not shown on gunsight, but ranging data is still fed to the gunsight when locked.
Radar use
1. RP-5 Radar Mode switch ... STAND BY (right click), radar takes 3 minutes to warm up (left side wall behind throttle) (Middle Finger Hat up/down)
2. When radar is warmed up, RP-5 Radar Mode switch ... FULL ON (right click) (left side wall behind throttle) (Middle Finger Hat up/down)
3. RP-5 Radar/Telemetry switch ... As needed: 1 for Low Altitude (below 2000 m AGL, disables search antenna) or 2 for High Altitude (above 2000 m AGL) (upper left on instrument panel)
4. RP-5 Radar Target Lock switch ... ON (up) (left side wall) (TDC press to toggle)
5. Radar should automatically lock closest target within 4000 m in High Altitude mode (locking area is shown as box on radar screen), or about 1200 m in Low Altitude mode
  - When locked, radar "bird" pipper will appear on the gunsight around the target (only in High Altitude mode), and LOCK lights above radar and next to gunsight should turn on.
  - "Bird" pipper gets wider as target gets closer, 1st hash = 2000 m, 2nd = 1000 m, 3rd = 300 m.
  - Distance to target will be shown on the ASP-5 Gunsight Target Distance gauge (left side of gunsight base)
  - No manual target selection or unlocking is possible, radar will only automatically lock closest target.
  - Range data is fed to the gunsite and used to calculate lead.

Guns -- 2x NR-30 30mm cannons, 73 rounds each
ASP-5 Sight Aiming Mode knob ... NR-30 (left side wall) (Gray Reset Hat backward)
Optical ranging
1. ASP-5 Sight Operational Mode switch ... OPTICAL (up) (left side wall) (Middle Finger Hat press to toggle)
2. ASP-5 Target Wingspan knob ... As needed for expected target (left side of gunsight base) (F-5E = 8.1 m, see built-in kneeboard pages for more wingspans)
3. ASP-5 Target Distance ... As needed (Top Hat Ring rotate), range in hundreds of meters (virtual throttle twist grip, indicator is gauge on left side of gunsight base)
4. ASP-5 Sight Cage/Uncage lever ... UNCAGE (left side of gunsight base) (Rear Thumb Button press to toggle)
5. Hold Electrical Cage button (Front Thumb Button press) to center the pipper so you can see to adjust range as needed, then release to return pipper to calculated position.
6. Put gunsight pipper on target and fire with Trigger.
Radar ranging
1. ASP-5 Sight Operational Mode switch ... RADAR (down) (left side wall) (Middle Finger Hat press to toggle)
2. ASP-5 Sight Cage/Uncage lever ... UNCAGE (left side of gunsight base) (Rear Thumb Button press to toggle)
3. Lock target on radar as detailed above. Range data will be fed to the gunsight from the radar.
4. Put gunsight pipper on target and fire with Trigger.

K-13A/R-3S (AA-2 Atoll) missiles - Rear Aspect, tailpipe only, non-maneuvering targets
1. ASP-5 Sight Aiming Mode knob ... GUIDED MISSILES (left side wall) (Gray Reset Hat forward)
2. Rocket Salvo Mode switch ... 1 RO (left side wall) (default is AUTO which will launch both missiles)
3. Put target in pipper and get tone.
  - Missile appears to automatically uncage when it starts tracking. Doesn't seem to be a way to unlock if you have multiple targets.
When you have tone, fire with Trigger.

General dogfighting tips:
- Don't pull too hard or you'll rip off your wings.
- Best turn speed seems to be around 800 kph?? Growling Sidewinder says 430 kts (800 kph).