1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201 - Ground - Cold Start

Cold Start -- Autostart cannot be customized, default takes 0m50s, probably faster than the manual start below
1. Right side switches:
  1. Right wall rear: All on (should only need to turn on 3 on bottom row next to the red knobs)
  2. Right wall middle: All on except FLIGHT REC (middle row), and CAM (bottom row)
  3. Right wall forward top: All on except WAVES
  4. Right console forward: All on except AUX INVERTER
2. Left side switches:
  1. Left wall forward: ENG APU, FIRE EXT, AUTO GEAR BRAKE ... ON
3. Center console switches:
  1. Top right corner: PITOT CLK. MIRROR HEAT ... ON
4. Throttle ... IDLE (Bottom Thumb button to toggle unlatched from STOP latch)
5. Engine Start button ... Press and hold for 4 seconds (left wall rear)
6. Engine should spool up to 3500 RPM 1 and 5050 RPM 2, ENGINE START warning light should go out.
7. Close, lock, and pressurize canopy:
  1. T7 up to toggle close
  2. T7 down to toggle lock (red levers on left wall forward, inboard lever forward is locked)
  3. Shift-T7 up to pressurize (red levers on left wall forward, outboard lever forward is pressurized)
8. After engine start:
9. FDS button ("NPP adjust") ... Press and hold for 5 seconds until HSI is fully aligned (instrument panel top, just left of center, next to yellow guarded DROP WING TANKS button)
10. PITOT lever ... MAIN (instrument panel top right)
11. Gunsight pipper ... ON (switch on right side of gunsight base, near the bottom)
12. (optional) Gunsight fixed net (fixed reticule) ... ON (switch on bottom of gunsight base, on right hand side) and adjust brightness (knob on bottom left of gunsight base)

Follow remaining steps in preflight checklist on following page.