1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

202 - Ground - Prefight, Performance Limits

Before takeoff (auto-started from cold; if hot start, some of these will already be set)
1. Check switches:
  1. Right side switches:
    1. Right wall rear: All on (should only need to turn on 3 on bottom row next to the red knobs)
    2. Right wall middle: All on except FLIGHT REC (middle row), and CAM (bottom row)
    3. Right wall forward top: All on except WAVES
    4. Right console forward: All on except AUX INVERTER
  2. Left side switches:
    1. Left wall forward: ENG APU, FIRE EXT, AUTO GEAR BRAKE ... ON
  3. Center console switches:
    1. Top right corner: PITOT CLK. MIRROR HEAT ... ON
2. PITOT lever ... MAIN (white lever on instrument panel top right)
3. Landing gear lever safety lock ... Up (above gear handle on left wall forward)
4. Flaps ... Takeoff position (T6 switch) (middle button on flaps control panel behind throttle)
5. Nose gear brake lever ... OFF (vertical) for taxi (left upper instrument panel)
6. SPRD/Countermeasures system (needed for both JATO boosters and chaff/flare launchers):
  1. SPRD System switch ... ON (right console middle)
  2. SPRD Drop System switch ... ON (right console middle)
  3. SPRD Drop Cover ... Open (red guard cover under throttle grip)
7. Radar power switch ... Standby/PREP (middle position) (right wall forward) requires 5 minutes to warm up
8. FDS button ("NPP adjust") ... Press and hold for 5 seconds until HSI is fully aligned (instrument panel top, just left of center, next to yellow guarded DROP WING TANKS button)
9. Armament:
  1. Gun RELOADING button 1 ... Press to arm gun
  2. Gunsight pipper switch ... ON (right side of gunsight base) and adjust brightness (knob on right side of gunsight base just above the switch)
  3. (optional) Gunsight fixed net ... ON (bottom of gunsight base) and adjust brightness (knob on lower left corner of gunsight base)
10. Radio / Compass switch ... RADIO (right wall forward, above red "+" radio channel selector)
11. Radio channel ... As needed (red cross dial on right wall)
12. Begin taxi, Rooskie brakes.
  - There is also a small amount of nosewheel steering with rudder pedals only, although the real plane does not have nosewheel steering.

Performance limits
- Full internal fuel: 2750 L (see Fuel Management kneeboard page for details)
- Emergency afterburner ... 3 minutes, then 30 sec cooldown.
- Landing gear max: 600 kph
- Touchdown max: 330 kph
- Drag chute max: 320 kph
- Speeds:
  - A/A missiles only (no drop tanks): Mach 2.05
  - Drop tanks (no A/G ordinance): Mach 1.6
  - A/G ordinance: Mach 1.0
  - Max range: 650 kph
  - Max endurance: 480 kph
- Gs:
  - Negative Gs: 5 seconds or less
    - If longer than 5 seconds, engine will flameout and need to be restarted. See other page.
  - A/A missiles only (no drop tanks): 7.0 G
  - A/G ordinance: 5.0 G
  - Small drop tank (450 L): 5.0 G
  - Large drop tank (800 L): 4.0 G
- Relative fuel consumption at altitudes:
  - 0 m:	100%
  - 3000 m:	80%
  - 6000 m:	65%
  - 9000 m:	60%
  - 11000 m:	55%