1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

303 - Flight - Navigation

NPP = HSI
KPP = ADI/Artificial Horizon

Navigation -- WIP needs verification
     VOR TACAN VORTAC VOR-DME NDB NDB-DME
ARC with ARC receiver
- ARC stations are not the same as NDB beacons, but may be co-located??
- You may need to be at least 2500 m altitude to receive ARC stations.
1. ARC/RSBN switch ... ARC
2. FDS button (where??) ... Hold for 2-3 seconds to align HSI compass??
3. Find sector/channel and sub-channel for ARC station (use built-in kneeboards and map)??
4. Set ARC sector/channel (e.g. 3-II) with knob.
5. Set sub-channel (e.g. 2) with button.
6. Set RADIO/COMP switch to COMP to hear beacon Morse code.
7. HSI compass should show direction to beacon with white needle that has a circle on the back and a solid (filled-in) pointer.
RSBN navigation (similar to VOR/TACAN)
- Not all airports have RSBN; it is not the same as TACAN or VOR.
- You may need to be at least 2500 m altitude to receive RSBN.
1. RSBN/ARC switch ... RSBN
2. RSBN channel knob ... Tune to RSBN channel (see built-in kneeboards or map??)
3. RSBN distance indicator (where??) should show distance to beacon.
4. Rotate the 3-K knob (where??) to set HSI pointer to runway heading. Fly to align beacon bearing with runway heading. There is no to/from indicator.
5. Set NAVIG/LDG switch to NAVIG. (PROCEED mode is used for cloud penetration with a guided descent speed and angle, see Chuck's.)
6. White bar in center of HSI compass shows deviation from radial (runway heading). Once on radial, turn to runway heading.
RSBN+PMRG landing (similar to ILS)
PMRG is military only, and will only be available at friendly coalition airports. It may also only be available for certain runways (as directed by airport traffic control) and in certain weather conditions (e.g. may not be available if there is good visibility or no wind).
1. When you are 25 km from landing airport and 600 m altitude, change RSBN receiver to PMRG channel.
2. RSBN Mode switch ... LDG
3. K and G flags on HSI should change from white to black when localizer and glideslope signals are received.
4. Artificial horizon will show localizer (horizontal) and glideslope (vertical) on small indicators at top and left. Lines show the approach path relative to your position, so chase the lines to get on path, as you would with ILS.