1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A/G - Unguided Bombs, Rockets, GROM

Stations on the plane are numbered 3-1-2-4 from pilot's perspective.

All
1. Master Mode switch ... GND
2. Weapon Mode switch ... NEUTRAL
3. Bottom ASP Mode switch ... AUT
4. ASP Pipper mode paddle switch ... MSL or GYRO??
5. Target Size knob ... As needed (10-12 meters if unknown)

Unguided bombs -- WIP (needs verification)
1. Weapon Selector knob ... "B" outer scale on the left: 1-2 for inner stations, 3-4 for outer stations, 1-4 for all stations
2. ASP Mode switches, top to bottom ... LNC, B, AUT, GYRO or MSL??
On center console
1. Tactical Drop cover ... Open
2. Tactical Drop switch ... On (up)
Radar panel (to right of right knee)
1. Radar power switch ... On
2. Radar low altitude mode ... Low Altitude Filter (Shift Middle Finger Hat press, cockpit switch in middle position)
3. Locked Beam ... On
Bomb run
1. Begin run at 4000 to 5000 m.
2. Dive steeply, 60 deg if possible
3. When pipper reaches target, press Red Button to pickle.
4. Pull up at 5 Gs or less to avoid ripping stores off wings.
5. Set up for next run by setting Weapon Selector knob to next set of pylons.

Rockets -- WIP (needs verification)
1. Air/Ground switch ... GROUND
2. Pylon knob ... Number of rockets per burst as desired: 4, 8, 16, or for S-24s either 1-2 or 3-4
3. Gunsight switches:
  1. LNC
  2. S
  3. AUT
  4. GYRO
4. Fire with Red Button.

KH-66 GROM -- Beam-riding A/G missile -- WIP (needs verification)
1. Air/Ground switch ... GROUND
2. Missile Mode switch ... NEUTRAL??
3. Pylon knob ... S-24 RKT 1-2
4. Gunsight switches:
  1. LNC
  2. S
  3. AUT
  4. GYRO
5. Radar:
  1. Low Alt switch ... Middle position
  2. Locked Beam ... ON
6. Dive and point pipper at target.
7. Fire with Red Button, missile beam-rides to pipper.