201 - Ground - Cold Start

Cold Start Checklist -- WIP needs verification
1. Canopy ... Close and lock (red lever on right side to forward position)
2. BATT switch ... ON (right console forward vertical panel)
  1. ALT1 and ALT2 switches ... ON (default)
  2. Inverter switch ... AUTO (default)
3. AVERT SON (Warning horn) switch ... ON (right console forward, 3rd switch from left)
4. Master Warning ... Press to reset
5. Start engine (left console forward):
  1. COUPE FEU switch ... ON (left) and cover closed
  2. POMPES B.P.G. and B.P.D. switches (Boost Pumps Gauche/Droit) ... ON (left)
  3. DEMAR cover ... Open
  4. When B.P. light on master caution panel goes out (1-2 seconds): Starter button ... Press for 1-2 secs
  5. DEMAR cover ... Close
  6. When RPM gauge reaches 300 RPM: Throttle ... IDLE (push throttle forward past detent)
  7. Engine will stabilize at 2900 RPM.
  8. NOTE: NEVER press starter button (under DEMAR cover) when engine is rotating at all.
6. Inverter switch ... REARM (momentary) and back to AUTO
  - SEC light on master caution panel should go out.
1. Master valve control switch ... ON (right console rear outboard on CABIN panel)
2. Gyro system knob ... GM (right console middle inboard)
3. Backup gyro switch ... ON (right console middle inboard, next to main Gyro system knob)
  - Gyros take about 2 min to align, CAP light on master caution panel will go out.
1. HORIZ SEC (backup artifical horizon) switch ... ON (right console forward)
2. EL POMPE (electro-pump) switch ... ON (right console forward)
3. ANEMO (probe heat) switch ... ON (right console forward)
4. RWR switch ... ON (right console forward)
5. RADAR EMISS switch ... Standby (center position) (right console forward)
6. HUD power switch ... ON (center position) (right console forward)
7. SERVO button ... Press to reset (left console forward vertical panel)
  - PA, LACET, TANG, ROUL, EMP, DIR lights on master caution panel should go out.
1. Standby horizon ... Uncage (instrument panel bottom center)
2. SOURIS button (shock-cone system) ... AUTO (press in) (center console between legs, top)
3. DIR button (NWS system) ... ON (press in) (center console between legs, top)
4. IFF panel ... Not simulated

Proceed with regular pre-flight checklist on next page.