202 - Ground - Preflight, Performance Limits

Preflight checklist (after hot or cold start)
1. If carrying drop tanks, set Fuel Transfer Sequence Selector switch (on fuel panel, center console top) to BIDONS ("cans"), otherwise set to LISSE ("smooth", clean/slick)
2. Lights ... As desired
  - Formation and anti-collision lights ... right console forward vertical panel outboard of master caution panel
  - Landing and taxi lights ... left wall forward outboard
  - Cockpit lights ... right console rear knobs
  - HUD brightness ... switches on top of gunsight base, and knobs on bottom of gunsight base
    - AUTO/MAN switch -- AUTO (forward) should make the sight brightness vary automatically based on ambient lighting, MAN (aft) should make the sight brightness controlled by knobs on bottom of gunsight base. Not sure if working correctly right now??
    - S/N/A switch -- A (aft) is all reticle lights off, N (middle) is normal operation, S (forward) is emergency operation if a bulb goes out
  - AOA, countermeasures, and G-meter lights ... small knob on bottom of stopwatch on upper left of HUD.
1. Flaps ... Half
2. Parking Brake ... Release (left console forward vertical panel, black/yellow striped handle)

Performance limits
Fuel:
	lbs	kg	lbs with internal	kg with internal
Internal	9354	4243	--	--
1x 1200 L centerline drop tank	2508	1138	11862	5381
2x 1200 L wing drop tanks	5017	2276	14371	6519
centerline + wing drop tanks	7525	3413	16879	7656

  - Jet fuel weight: 1 L = 0.81 kg, 1 kg = 1.23 L
- Landing Gear: 240 kts
- Flaps:
  - Half: 300 kts
  - Full: 225 kts
- Combat slats and flaps:
  - Auto slats only: 470 kts or Mach 1.1
  - Combat slats and flaps: 335 kts or Mach 0.85
- Brake chute: 210 kts
- Max speed: Approx 2.3 Mach at 45000 ft before wings ripped off
- G limits:
  - Subsonic: -3 to +7.2
  - Supersonic: -3 to +6
- Negative G: 15 sec
- Max speed:
  - Below 20,000 ft: 700 kts IAS
  - Above 20,000 ft: 750 kts IAS
  - Mach limit: 2.1
- Spin recovery: Neutralize controls, then apply opposite rudder.
- Maximum flight endurance with air refueling: 6 hours (due to oil consumption)