304 - Flight - Radios, Countermeasures, RWR

Radios
COM1??	TRAP 136	V/UHF	118.0 to 143.975 MHz / 225.0 to 399.975 MHz	"Green" radio. Preset channels or manual tune.
COM2??	TRAP 137B	UHF	225.0 to 399.975 MHz	"Red" radio. Preset channels only.

- Radio volume panel is on left console forward inboard, next to left knee.
- Select active radio with AMPLI knob on volume panel??
TRAP 136 ("Green" radio)
- Control panel is on left console far forward.
- Mode knob:
  - AR -- OFF
  - PAL -- ON, using selected frequency
  - PAL+G -- Same as PAL, but also monitoring Guard (121.5 MHz).
  - F1 -- Not used
  - H -- Not used
- Frequency selector knob:
  - M -- Manual tuning, uses frequency shown in window above.
  - P -- Preset channel, uses channel shown in window above left.
  - G -- Guard (121.5 MHz)
TRAP 137B ("Red" radio)
- Control panel is on left console rear, behind radar stick.
- Mode knob:
  - AR -- OFF
  - M -- ON, using selected channel
  - F1 -- Not used
  - H -- Not used
- Change channel with black knob, selected channel is shown in window.

Countermeasures
- Dispense countermeasures with Top Hat forward or back (either direction does the same thing) (actual button in cockpit is on the left wall, in front and above the throttle handle)
- Set countermeasures type and mode on countermeasures control panel, left side of HUD:
  - Recommended: BOTH and SGL
  - CHAFF/FLARE/BOTH switch -- Dispenses chaff only, flares only, or both.
  - Program selector knob:
    - OFF -- Countermeasures system disabled.
    - SGL -- One countermeasure released per side
    - MULT -- Launches one burst?? of countermeasures as defined in the ME.
    - PRGM -- Launches multiple bursts?? of countermeasures at salvo interval?? as defined in the ME.
- Normal load is 15 flares on left side and 30 chaff on right side.
- Countermeasures program is set up in the mission editor. Default program??:
  - Chaff burst count: 1
  - Chaff burst interval: 0.05s
  - Chaff salvo count: 1
  - Chaff salvo interval: 1.0s
  - Flare burst count: 1
  - Flare burst interval: 3.0s

RWR system
- Lights at top are threat type. Left to right:
  - Pulse-modulated radar lock -- Indicates a STT lock on your plane
  - TWS lock -- Indicates a TWS lock on your plane
  - CW lock -- Indicates a continuous wave lock on your plane, which is usually a missile guidance radar, meaning a missile is in the air
- 4 directional lights around the airplane diagram show the direction to the strongest radar source (not necessarily the closest, or the most dangerous).