402 - A/A - Gun, Magic, Super

Fence In
Master Arm ... ON (B2 button to toggle)

30 mm cannon -- 2x DEFA 553, 150 rounds per gun
1. Press Trigger to fire. Trigger always fires guns as long as Master Arm is ON.
2. (Optional)Press Throttle C+SW/M button to enter dogfight mode.
3. :
Available radar ACM modes (automatic lock, 10 nmi range):
- WSC (Dish Hat) Forward: Boresight/Vertical scan
- WSC (Dish Hat) Backward: Cycles BAH/BA2 horizontal scan mode (BAH = High PRF, BA2 = Medium PRF (special PRF mode only available in BA2))
- WSC (Dish Hat) Press: Unlock target or exit other mode

Matra R.530
- When both missiles are selected, firing priority is as follows:
  - Locked missile has priority.
  - If both are locked, IR missile has priority.
  - If both are same seeker type, left missile has priority.
- R.530 IR missile has 20 minutes of coolant, and takes 20 seconds to cool the seeker head. Cooling begins when Master Arm is on and missile is selected on armament panel??

R.550 Magic IR missiles
1. Press Gray Reset Hat forward ("CNM Switch down") to select Magic missiles.
2. On PPA (above right knee):
  1. Ensure Magic Standby button shows "P". If not, press to start cooldown (30 seconds). You have 90 minutes of coolant. Subsequent stop/starts take 10 minutes worth each.
  2. Set pylon if desired: I = Auto (default), G = Left, R = Right
3. Missile seeker search mode is determined by button on PCA (above left knee):
  - If MAG: Search modes are Vertical Wide Search and Vertical Narrow Search.
  - If MAV: Search modes are Horizontal Wide Search and Vertical Narrow Search.
1. In both cases, Vertical Narrow Search is indicated with a dashed box on the upper part of the HUD.
2. Front Thumb Button unlocks target (without resetting HUD mode), and toggles seeker search mode.
3. When using with a radar lock, press Rear Thumb Button (Uncage button) to slave seeker to target.
4. Press and hold Trigger to fire.
  - Engine RPM will drop for a few seconds to prevent flameout from exhaust gas ingestion.
Available radar ACM modes (automatic lock, 10 nmi range):
- WSC (Dish Hat) Forward: Boresight/Vertical scan
- WSC (Dish Hat) Backward: Cycles BAH/BA2 horizontal scan mode (BAH = High PRF, BA2 = Medium PRF (special PRF mode only available in BA2))
- WSC (Dish Hat) Press: Unlock target or exit other mode

Super 530D SARH missiles
1. Press Gray Reset Hat press ("CNM Switch neutral") to set PCA weapon select.
2. On PPA (above right knee):
  1. Ensure S530 Standby button shows "P". If not, press to start warm-up (45 seconds).
  2. Set pylon if desired: I = Auto (default), G = Left, R = Right
  3. 530D/Rockets/Guns Firing Mode Selector button ... TOT for 2 missiles per launch, PAR for 1 missile per launch
3. On PCA (above left knee):
  1. Select 530 button for missiles. Button will show yellow "S".
4. Lock target in TWS (PID on radar) or STT (PIC on radar).
5. Range symbology is shown on right of HUD. Max, NE zone, min, and target range.
6. When in range, press and hold Trigger to fire.
  - If in TWS (PID) mode, radar will automatically lock in STT before launching missile.
  - Engine RPM will drop for a few seconds to prevent flameout from exhaust gas ingestion.
1. When done with missiles, press 530 on PCA panel so the "S" goes away.
2. Set HUD back to NAV mode with Weapons System CMD AFT (Dish Hat down)
Available radar ACM modes (automatic lock, 10 nmi range):
- WSC (Dish Hat) Forward: Boresight/HUD Spiral (shows SVI), or Flood if missile is in the air (use to quickly re-lock on a target that broke lock)
- WSC (Dish Hat) Backward: Cycles BAH/BA2 horizontal scan mode (BAH = High PRF, BA2 = Medium PRF (special PRF mode only available in BA2))
- WSC (Dish Hat) Press: Unlock target or exit other mode