501 - A/G - Guns, Rockets, Bombs

Fence In
Master Arm ... ON (B2 button to toggle)

Mixing weapons
In reality, mixed bomb/rocket loadouts were not authorized, but they can be used in the game.

Special notes
Mirage F1CE does not have a radar altimeter. For ground reference, set baro altimeter to QFE for the target area. Keep your standby baro altimeter set to QNH for reference. To estimate QFE:
  1. If you have the target elevation (i.e. from the map) simply wind back your altimeter to subtract that elevation from your current altitude.
  2. If you don't have the target elevation, calculate QFE by starting with QNH in millibars or hectopascals (ISA = 1013.25 mb or hpa). The altimeter is set to QNH by default. Then subtract 1 mb per 30 ft or 10 m. (Slighly more accurate: 1.1 mb per 30 ft, 1.2 mb per 10 m.)

Guns
1. Press CAN.S ROQ button on armament control panel (right console forward).
2. Press Trigger to fire.
Gun firing dipper switch sets whether engine will automatically reduce RPMs while firing to prevent stall from gas ingestion. Recommended to leave ON.
Sight depression settings
10 deg dive, 320 kts, 2500 ft release: 44 mrads

Rockets
1. Press CAN.S ROQ button on armament control panel (right console forward)
2. Use BOMB/ROQ switch to select station:
  1. IN -- Inboard stations only
  2. 1+2 -- Inboard and outboard stations
  3. EX -- Outboard stations only
3. Set quantity with salvo switch:
  1. SALV -- Rockets will fire continuously as long as pickle is held. (Note: Must press and hold pickle button, not sure if that is intentional behavior...)
  2. CPC -- Rockets will fire in bursts of 6 per pod per pickle press. The number fired per press is set in the Mission Editor, default is 6 for F1 (36-shot) pods and 1 for F4 (18-shot) pods.
4. Press Red Button to fire.
Sight depression settings
10 deg dive, 320 kts, 4000 ft release: 56 mrads

Bombs
1. Select bombs.
  1. For fuselage bombs only, press BOMB FUSE button on armament control panel.
  2. For wing bombs only, press BOMB VOIL button on armament control panel.
  3. For both, press both.
  4. If fuselage bombs are selected, they will always drop.
  5. If wing bombs are selected, use BOMB/ROQ switch to select station:
    1. IN -- Inboard stations only
    2. 1+2 -- Inboard and outboard stations
    3. EX -- Outboard stations only
2. Set fuzing with fuzing switch:
  1. INERT -- Safe
  2. RET -- Delay
  3. INST -- Instant
3. Set quantity with salvo switch:
  1. SALV -- Bombs will drop in a continuous string as long as pickle is held.
  2. CPC -- Bombs will drop one per pickle press.
4. Press Red Button to drop bombs.
IRL, airbrakes are not authorized to be deployed when bombs release, but they can be used in the game.
Sight depression settings
20 deg dive, 400 kts, 1700 ft release: 106 mrads