1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Radios, Datalink setup, Countermeasures, Jettison

Radio setup and tuning
Band	Frequency range	Modulation	T/R	Notes
COM1?? -- ARC-186(V)
VHF	108.000 to 115.975 MHz	AM	R
VHF	116.000 to 151.975 MHz	AM	T/R
COM2?? -- ARC-164(V)
UHF	225.000 to 399.975 MHz	AM	T/R
COM3?? -- ARC-201D
VHF	30.000 to 87.975 MHz	FM	T/R	2x, FM1 and FM2
COM4?? -- ARC-220
HF	2.000 to 29.999 MHz	FM	T/R

Preset frequencies using EUFD:
EUFD cannot tune IDM or SINCGARS channels.
1. Press P button to show preset channel list.
2. Use RTS rocker to select radio. Selected radio is what you will transmit on.
3. Use WCA rocker to select preset channel from list, for selected radio.
4. Press ↵ (Enter) to tune selected radio to preset.
5. Press 🗘 (Swap) to switch primary and secondary frequencies for selected radio.
EUFD symbols:
◀ ▪	You have selected this radio for voice transmission.
▪ ▶	The other crewmember has selected this radio for voice transmission.
◀ ▶	Both crewmembers have selected this radio for voice transmission.
▪ ▪	Neither crewmember has selected this radio for voice transmission.
◆	You have selected this radio for IDM transmission.
◆	The other crewmember has selected this radio for IDM transmission.
◼	Both crewmembers have selected this radio for IDM transmission.
*	Squelch on.
Manual frequencies on COM page (COM OSB):
When radio is tuned to a manual frequency, IDM cannot be used on that radio.
1. Press COM OSB, then MAN OSB.
2. Press L1-L4 OSB to select VHF, UHF, FM1, or FM2 radios. Press R1 or R3 to select HF Receive or HF Transmit frequencies respectively.
3. Enter frequency on KU (Keyboard Unit) and press ENTER to set.

Countermeasures setup
1. Radar and laser threats are displayed on the ASE page, which can be set to pop up automatically ("Autopage") when threats are detected or tracking you.
2. Missile launches are displayed on the CMWS control box, which is not integrated with the ASE.
3. Chaff is controlled by ASE system and page, Flares are controlled by CMWS system and control box.
4. On CMWS control panel (PLT front right canopy frame):
  1. Power knob ... ON
  2. AUDIO and LAMP knobs ... As desired
  3. ARM/SAFE switch ... ARM
  4. CMWS/NAV switch ... CMWS (sets audio to CMWS; NAV is ADF receiver audio)
    - Because the CMWS is a post-production mod, it uses the ADF audio channel, hence the switch.
  1. BYPASS/AUTO switch ... BYPASS??
2. Screen shows remaining Flares and Chaff, arrows show direction to threat, D=Dispensing, R=Ready.
3. To set up Chaff program: ASE page -> UTIL -> L1-L5 OSBs.

Jettison
1. Stores Jettison Panel is on left console (both crew stations).
2. Press ARM buttons for stations you want to jettison, then press JETT button.
3. Or, use the Emergency Jettison switch on the collective to jettison all external stores.