1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

302 - Flight - Navigation

General info
- 99 waypoints (1W-99W), 99 target points (1T-99T), 99 control points (1C-99C)??
  - Control points are used for battlefield graphics??
- 3 routes. How many points per route??

Add/Edit a waypoint
1. HSD page > NAV SETUP OSB > NEW WPT OSB (used both for adding new and editing existing)
2. Should default to next available waypoint number?? To create a new waypoint, follow the steps below. To edit an existing waypoint, press the WPT OSB (L1 OSB), press CLR on the keyboard (center console) and enter desired waypoint (e.g. "7W"), and press ENTER. That should load that waypoint's data on the screen.
3. Press POS OSB to begin entering location.
4. Larger grid square should be auto-populated, enter the rest of the MGRS coordinates in 8-digit format on keyboard (center console) and press ENTER.
  - You can toggle MGRS/lat-long entry by pressing UTM LAT/LON OSB (R4 OSB).
1. Waypoint will automatically be set to ground elevation at that location in meters (or feet if using lat/long??), change if needed with ELEV OSB (L4 OSB).
2. Optional: To make waypoint available as a PREPOINT for MMS cueing, box PREPOINT OSB (R3 OSB)
  - You also can add waypoints to the prepoint list directly through the MMS PAGE > PPT OSB even if they are not set as a prepoint on this page.
Press STORE OSB to save.

Routes
Create route
TODO
Edit route
TODO