1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A/G - MMS (Mast Mounted Sight)

MMS use -- WIP
1. MMS Mode knob ... PREPT or FWD (CPG instrument panel lower left)
2. Select MMS page ... press MMS OSB (CPG MFD)
3. When initially powered up, will show TIS HOT at bottom of MFD until TIS cools down.
4. Press Manual/Slave button (Collective Ministick press) to toggle manual (slew with Ministick) or slaved to target or other point.
  1. If in FWD mode, Manual/Slave will toggle between manual slewing and pointed forward.
  2. If in PREPT mode, Manual/Slave will toggle between manual slewing and pointed at target or other point.
5. Change pre-set laser codes:
  1. Press CODE LIST button (CPG instrument panel upper left, next to MFD) to toggle LASER CODES page.
  2. Press OSB next to code you want to change.
  3. On keyboard (center console), press CLR, then enter new code, then ENTER.
  4. Press CODE LIST button again to return to previous MFD page.
6. Arm laser with switch left of MFD.
7. Change MFD brightness/contrast with rocker switches left of MFD. Switches under the rockers control whether they are automatically controlled.
8. Switches under CPG MFD:
  1. ALFGL ... not functional (Automatic Low Frequency Gain Limiting)
  2. WPN/ASE ... Selects WPN or ASE pages on MFD. Press WPN repeatedly to cycle main WEAPONS PAGE, left pylon Sparse Weapon Page, and right pylon Sparse Weapon Page.
  3. IDM/INIT ... Selects IDM (not functional) or Initial pages on MFD
  4. L2MUM ... not functional
  5. TIS INTEG ... not functional
  6. LMC ... (Linear Motion Compensator) Turns on automatic ground locking/stabilization with laser range??
  7. ALE ... Automatic Leveling, not functional
9. Select Ranging-only mode or Designating with a laser code: Press L1 OSB to cycle RNG, then through all the laser codes, and back to RNG.
10. Store a target:
  1. Lase target to get range?? Not sure if you have to do that first...
  2. Press "Target Designate/Locate Function" button, bottom of MFD should say TGT LOC.
  3. Lase target continuously for about 5 seconds.
  4. Press L4 to STORE or L5 to REJECT target. Targets are stored in target points in reverse order (starting at 99T) to avoid overwriting pre-planned points.
  5. See stored targets with HSD OSB > NAV SETUP OSB > TGT LIST OSB, then use PREV PAGE/NEXT PAGE OSBs.
11. Offset lasing/designation:
  1. Point track button (Collective Middle Hat right), then point track button again. Now slew will move a small cross hair independently around the screen. Point track button again to jump the MMS to the new target. Point track button again to jump the MMS back to the original target.
12. Area track and automatically lock targets:
  1. Press Area Track button to ground stabilize. Put crosshairs near ground target. Area Track button again to get movable diamond cursor?? Move cursor over target to automatically lock it?? Once locked, press Point Track button to jump MMS to that target.
13. Tested max laser range is just over 27,000 m!
14. Get target grid location: -- WIP needs verification
  1. Point MMS at target.
  2. Press Target Designate/Locate button (Collective Trim Hat down).
  3. Lase target (maybe for several seconds??)
  4. Target grid location shown in lower left of MFD. STORE and REJECT OSBs give options to store the target as a target point (nnT) or exit Target Location mode.

Prepoint mode
1. MMS Mode knob ... PREPT (instrument panel lower left, above Copilot's left knee)
2. Press Manual/Slave toggle (Collective Ministick press) to slave MMS to the prepoint waypoint.
3. Prepoint location is shown on Copilot's MMS PAGE as a dashed crosshair. (Does not show on Pilot's MMS PAGE.)
4. PPT OSB (R2 OSB) shows currently selected prepoint. If blank, no point is selected.
5. Prepoints can be waypoints (nnW), targets (nnT), or control points (nnC).
6. To select a point, press PPT OSB to bring up PPT list. Within 5 seconds, begin entering a waypoint, target, or control point ID on the keyboard, then press ENTER.
7. Press PPT OSB to cycle down through the list.
8. When a PPT is boxed in the list, either wait 5 seconds for the list to close, or close it by pressing the MMS OSB (B3 OSB).