1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

504 - A/G - Rockets and APKWS

Fence In:
- Master Arm ... ARMED
- Laser ... ARM

Hydra 70 Rockets -- 70 mm rockets, M261 launcher, 7x rockets/pod -- WIP
1. Select rockets with Gray Reset Hat left/right, which will show Sparse Weapon Page.
2. Set up rocket options:
  - MODE OSB ...
    - SINGLES/SINGLES -- One rocket per Trigger press, alternating pods.
    - RIPPLE/SINGLES -- Fires continuously while Trigger is held, alternating pods.
    - SINGLES/PAIRS -- Two rockets per Trigger press, one from each pod simultaneously.
    - RIPPLE/PAIRS -- Fires continuously while Trigger is held, from both pods simultaneously.
  - FUZE/CUE OSB ... Not implemented in DCS?? Setting doesn't matter??
  - ZONE OSB ... Cycles ALL, A, or B zone to fire.
Fire with Trigger 2nd Stage.

APKWS
1. Set laser code on rockets in built-in kneeboard page. Can only be changed on the ground (weight on skids), but can be anywhere, not just at a friendly base.
2. Copilot: Set MMS laser code on MMS PAGE ... L1 OSB to cycle codes
3. Set up rockets as above, SINGLES/SINGLES mode recommended.
4. APKWS don't show any lock indication, they just home on the dot immediately when they see it, so in effect, you're always shooting in LOAL mode.
5. APKWS seeker has about a 30 deg FOV (+/-15 deg off nose in all directions).
6. Tested range from 50 ft hover: 1.5 km min to 9.5 km max.
APKWS range table -- Tested at sea level in ISA conditions from 50 ft hover
Target range	Loft angle	When to start lasing
1.5 km to 3.0 km	5 deg (hover)	Immediately
3.0 km to 4.5 km	5 deg (hover)	5 sec
4.5 km to 6.0 km	5 deg (hover)	10 seconds
6.0 km to 8.5 km	10 deg	10 seconds
8.5 km to 9.5 km	15 deg	15 sec

MMS commands on Collective (basic commands only)
- Slew ... Ministick
- Toggle Manual/Slaved mode ... Ministick press
- Toggle Narrow/Wide FOV ... Middle Hat up/down, press repeatedly to cycle zoom within each FOV
- Point track ... Middle Hat right, press repeatedly to use Offset Point Track
- Toggle TV/TIS (IR) ... Middle Hat left

Pilot AI commands
- Toggle Pilot AI on/off ... Trim Hat press
- Toggle Pilot AI HUD display on/off ... Shift-Trim Hat press
- Pilot AI hover ... Trim Hat down
- Pilot AI turn to MMS ... Trim Hat up
- Pilot AI slide left/right in hover ... Trim Hat left/right to set speed (to stop, press Trim Hat down to hover)
- Pilot AI altitude up/down ... Shift-Trim Hat up/down
  - Pilot AI use radar alt for setting altitude (fine control in hover)... LAlt-F
  - Pilot AI use use baro alt ... LAlt-A
- Pilot AI turn left/right ... Shift-Trim Hat left/right

Rocket zones
- Rocket pods have 2 zones: A and B
  (left) Zones: ● = A, ○ = B; (right) Firing Sequence
- Zone A ... 4 total: Top and bottom rockets.
- Zone B ... 3 total: Middle rockets.
- Different rockets can be loaded in each zone, and zones can be selected with ZONE OSB.