1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

505 - A/G - AGM-114K Hellfire

Fence In:
- Master Arm ... ARMED
- Laser ... ARM (CPG instrument panel left)

Tested ranges from 50 ft AGL hover -- Min laser range is <50 m, max is 27+ km
Mode	Traj	Min	Max
LOAL	HI	4.0 km	9.0 km
LOAL	LO	4.0 km	9.0 km
LOAL	DIR	2.0 km	9.0 km
LOBL	n/a	500 m	9.0 km

AGM-114K Hellfire II semi-active laser, self-designating -- WIP
- Hellfires can only be mounted on the left pylon if the right pylon is empty or also has Hellfires. To change loadout, change right pylon first.
- Laser Hellfire trajectories -- There are 4 trajectories: LOBL, LOAL DIR, LOAL LO, and LOAL HI. If the missile sees the laser designation at the time of launch, it will always use LOBL, otherwise it will use LOAL DIR/LO/HI. Select trajectory with DELVRY OSB on Pilot Sparse Weapons Page.
1. Set MMS laser code:
  1. On MMS page, press L1 OSB to cycle through RNG mode, then all the pre-set laser codes.
  2. Change pre-set laser codes by pressing CODE LIST button to toggle LASER CODES page. Press OSB next to code you want to change, press CLR on keyboard (center console), enter new code, then press ENTER. Press CODE LIST button again to return to previous page.
2. Set missile laser code:
  1. Master Arm switch ... STBY (must be in STBY to change codes??)
  2. Any MFD, go to WEAPONS PAGE (Pilot: Gray Reset Hat forward; Copilot: WPN/ASE switch up)
  3. Current PRI/ALT codes are shown in the middle.
  4. Change codes by pressing PRI/ALT CODES OSB, then enter A-H on keyboard (center console) and press ENTER for PRI, enter A-H again and press ENTER for ALT.
  5. Master Arm switch ... ARMED
3. Select missile with Gray Reset Hat left/right toward pylon you have Hellfires on.
4. CONSTR OSB ... NORMAL (ORIDE allows you to fire when out of constraints)
5. LAUNCH OSB ... MAN (I think this should be NORM?? but NORM causes the second missile to have the wrong laser code or other problems, and setting may have to be cycled to fix, suspect a bug...???)
  - When you first enable the missile, it may say SEL as it warms up. When ready, it will show RDY.
1. DELVRY OSB ... Press to cycle LOBL, DIR, LO, HI (LO, HI, and DIR are LOAL modes)
2. VID OSB ... OFF, TV, or TIS as desired to show underlay of MMS video
3. Point MMS at target.
4. Press and hold Collective Trigger or Joystick Red Button to lase.
5. When constraints box is solid, indicating missile sees the laser, press and hold Trigger 2nd Stage until missile fires.
  - If you let go early, it may cause a hangfire??

MMS commands on Collective (basic commands only)
- Slew ... Ministick
- Toggle Manual/Slaved mode ... Ministick press
- Toggle Narrow/Wide FOV ... Middle Hat up/down, press repeatedly to cycle zoom within each FOV
- Point track ... Middle Hat right, press repeatedly to use Offset Point Track
- Toggle TV/TIS (IR) ... Middle Hat left

Pilot AI commands
- Toggle Pilot AI on/off ... Trim Hat press
- Toggle Pilot AI HUD display on/off ... Shift-Trim Hat press
- Pilot AI hover ... Trim Hat down
- Pilot AI turn to MMS ... Trim Hat up
- Pilot AI slide left/right in hover ... Trim Hat left/right to set speed (to stop, press Trim Hat down to hover)
- Pilot AI altitude up/down ... Shift-Trim Hat up/down
- Pilot AI turn left/right ... Shift-Trim Hat left/right