1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

105 - Controls - Gunner - Collective Grip Alpha-L
U=Up, D=Down, F=Forward, B=Backward, L=Left, R=Right, P=Press, S-*=Shift-*, L-*=Long-*

Trigger
- P1: Alternate Cursor enter
- P2: --
Flip-down Trigger
P: --
Top hat -- FCR Scan switch, FCR Cued Search button, Missile Advance button, (shifted) FCR Scan Size hat
- U: FCR Scan switch forward (S-SCAN, single sweep)
- D: FCR Scan switch back (C-SCAN, continuous scanning)
- L: Missile Advance (only used with Manual Hellfire missile sequencing)
- R: --
- P: FCR Cued Search button (slew FCR to detected emitter)
- S-U: FCR Scan Size Zoom (15 deg arc)
- S-D: FCR Scan Size Medium (45 deg arc)
- S-R: FCR Scan Size Wide (90 deg arc)
- S-L: FCR Scan Size Narrow (30 deg arc)
Middle hat -- Sight Select hat, (shifted) FCR Mode hat
- U: Sight Select HMD (IHADSS)
- D: Sight Select LINK (sets FCR or TADS to LOS of TADS or FCR, depending on which is selected)
- L: Sight Select FCR
- R: Sight Select TADS (not active in pilot's station)
- S-U: FCR GTM (Ground Target Mode)
- S-D: FCR ATM (Air Target Mode)
- S-R: FCR RMAP (Radar Map mode)
- S-L: FCR TPM (Terrain Profiles Mode)
Ministick -- Cursor Controller/Enter, Cursor Display Select button
- Axes: Cursor controller
- P: Cursor enter
- S-P: Cursor Display Select button (toggles cursor between MFDs)
- U/D/L/R: Searchlight
- P: Searchlight switch STOW -> OFF -> ON
- S-P: Searchlight switch ON -> OFF -> STOW
Thumb hat -- Comms
- L: (SRS radio 1 PTT)
- R: (SRS radio 2 PTT)
- D: (SRS radio 3 PTT)
- S-L: Radio 1 PTT (opens comms menu for radio 1)
- S-R: Radio 2 PTT (opens comms menu for radio 2)
- P: (VoiceAttack PTT)
- S-P: (VoiceAttack center mouse cursor)
Index finger hat -- NVS Select, (shifted) Stabilator control
- U: NVS Select switch TADS
- D: NVS Select switch PNVS
- P: Boresight/Polarity switch PLRT (toggles FLIR polarity; switch to B/S is no function)
- S-U: Stabilator Control nose down
- S-D: Stabilator Control nose up
- S-P: Stabilator Control auto mode (also disables NOE/A mode if active)
Red Button -- Countermeasures Chaff
P: Chaff
Black Button -- Countermeasures Flares
P: Flares
Scroll Wheel -- Kneeboard
- P1: Kneeboard toggle
- P2: --
- F: Previous page
- B: Next page
Brake lever
- Axis: --
- P: --
Pinky button
- P: Wheel brakes (toggle)
- S-P: Tail Wheel lock/unlock