1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201 - Ground - Cold Start

General French stuff
M = Marche = ON/START
A = Arrêt = OFF/STOP
G = Gauche = LEFT
D = Droit = RIGHT
L = Lent = SLOW
R = Rapide = FAST

Manual Cold Start -- WIP
1. Cockpit doors ... Close (RCtrl-C)
2. Battery switch ... ON (front instrument panel bottom right)
3. Alternator switch ... ON (front instrument panel bottom right)
4. Generator switch ... ON (front instrument panel bottom right)
5. UHF radio mode knob ... FF (front center console)
6. NADIR mode ... VEILLE (initialize) (center angled console)
7. Fuel Pump switch ... ON (front angled instrument panel)
  1. Wait 20 seconds for fuel pump to prime
8. Starter switch ... M (On) (front angled instrument panel)
9. Wait for engine to reach idle (25,100 RPM) (25s).
10. Rotor Brake lever ... RELEASE (full forward) (large red handled lever on ceiling)
11. Fuel Flow lever ... Slightly forward until rotor begins to rotate (small yellow handled lever on ceiling)
  - Turbine RPM should be at about 29,000 for this.
1. When rotor RPM needle matches engine RPM needle: Fuel Flow lever ... Slowly forward all the way as engine and rotor spool up.
2. Pitot heat switch ... ON (front instrument panel bottom left)
3. Trim switch ... ON (enables trim hat) (front instrument panel bottom)
4. Magnetic brake switch ... ON (enables stick centering trim) (front angled instrument panel top)
5. Gyro Knob ... GM (begins gyro alignment, 60s) (copilot instrument panel bottom)
6. Autopilot master switch ... ON (front angled instrument panel bottom)
7. Autopilot pitch, roll, and yaw switches ... ON (front angled instrument panel bottom)
8. Artificial horizon ... Uncage
9. Standby artificial horizon ... Uncage
10. Radar altimeter ... ON and set bug as desired

Proceed with pre-flight checks on next page.