1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

302 - Flight - Artificial Horizon, SAS, Autopilot, Autohover

Artificial Horizon modes
Mode knob:
  - ART -- Artificial horizon only (no needles)
  - VIS -- VISEUR, needles point to camera target
  - VHF -- Needles point to ADF source
  - DOP -- Needles show doppler ground speed forward/backward and left/right

SAS - Stability Augmentation System
1. SAS switches are on bottom right of instrument panel.
2. SAS channels are controlled with individual pitch/roll/yaw switches.
3. SAS engages at 120 kph.
4. Autopilot and autohover (below) require SAS to be enabled.

Autopilot
1. Autopilot switches are on bottom right of instrument panel.
2. Autopilot power switch ... ON
3. Autopilot switch positions:
  1. Up -- Altitude Hold, holds current altitude
  2. Neutral -- Autopilot off
  3. Down -- Speed Hold, holds 120 kph??
4. When Altitude Hold or Speed Hold mode is engaged, collective will control speed or altitude, respectively.

Autohover
1. To autohover:
  1. Ground speed < 18 kph
  2. Roll and pitch angle < 30 deg
  3. Vertical speed < 60 m/min
2. Set Artificial horizon mode to DOP, needles will show relative ground speed forward/back and left/right.
3. Press autohover button to engage autohover.
4. When autohover is engaged, cyclic cannot be moved.
5. Use autoslave button to point helicopter at Viviane camera target (useful for HOT missiles).