1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

303 - Flight - Radios, Radio Navigation

Radio setup and tuning
COM1	TRAP 138A	VHF	118.000 to 143.975 MHz	AM
COM2	TRA 6031	UHF	225.000 to 399.975 MHz	AM
COM3	TRC 9600 PR4G	HF	30.000 to 87.975 MHz	FM	Preset channels only

Radio locations
- SA342L (20mm/rockets) and SA342Mistral
  - VHF -- Center console top
  - HF -- Under copilot dashboard
  - UHF -- Center console rear
- SA342M (HOT3) and SA342Minigun
  - VHF -- Center console front
  - HF -- Center console middle
  - UHF -- Center console rear
All
1. Select active radio by clicking (pressing inward) the volume knob for VHF, UHF, or FM1 on the radio panel (center console top).
2. Set volume by turning volume knobs.
VHF AM radio
Mode knob:
  - A = Off
  - M = On
  - Sil = Squelch off
  - TEST = Test, sounds continuous tone
Tune with knobs.
UHF AM radio
Mode knob:
  - 0 = Off
  - FF, NA, SV, DL, 6, EN = ON
Tune by entering frequency with number keys, then press VLD XFR button.
HF FM radio
Mode knob:
  - AR = OFF
  - TRAFFIC, CH.OTAN, REL = ON
  - TST = Test, sounds continuous tone
Select preset channel with channel knob. Channels are defined in the mission editor.

Navigate to NDB with ADF
1. ADF mode knob ... AF
2. ADF tone switch ... ON
3. Tune frequency with knobs on left or right frequency window.
4. Set TFR switch (between frequency windows) left or right to select that frequency.
5. ADF needle (single-line arrow) in HSI compass points to NDB bearing.