1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A/G - Viviane and ATHOS sights, HOT3 missiles

Master Arm ... ON (B2 button, or switch on instrument panel under radar altimeter)
TV system ... ON

SA342M -- Viviane TV/IR sighting system
FOV: 120 deg left/right, 25 deg up, 20 deg down
Turn sighting system on (copilot seat, VCB = Video Command Box next to TV display):
1. VCB Power Selector knob ... M (ON) (VCB next to TV)
2. VCB IR Power Selector knob ... M (ON) (VCB next to TV)
3. VCB Mode Selector knob ... Pil for manual tracking, Ass to auto-follow moving targets (VCB next to TV)
4. TV On/Off switch ... ON (toggle switch under TV screen)
5. Controls:
  1. Slew sight with TDC ministick
  2. Laser ranging
  3. Ground stabilization
  4. Zoom toggle
  5. TV/IR mode
  6. White/black crosshairs

SA342L -- ATHOS optical periscope
1. Controls:
  1. Slew sight with TDC ministick
  2. Change crosshair for range estimation
  3. Ground stabilization
  4. Zoom 1x and 4x?
2. Periscope sight has 3 ranging reticles. The stadia marks (black lines) subtend the following:
  1. Wide (GC) zoom:
    1. "3" -- 10 mils
    2. "2" -- 4 mils
    3. "1" -- 2.5 mils
  2. Narrow (PC) zoom (4x?):
    1. "3" -- 5 mils
    2. "2" -- 2 mils
    3. "1" -- 1.25 mils
  3. Range formula: TargetSize / (StadiaLines * MilsPerStadia) * 1000 = Range
    1. Example: BMP-2 is two stadia lines long in narrow zoom, with 1.25 mil reticle. 6.7 / (2 * 1.25) * 1000 = 2680 m
Target	Length (m)	Width (m)	Height (m)
BTR-80	7.7	2.9	2.4
BMP 2	6.7	3.2	2.5
ZSU-23-4	6.5	3.1	2.6 hull, 3.6 with radar elevated
T-72	7.0 hull, 9.5 with gun forward	3.6	2.2

SA342L and SA342M -- HOT3 missiles -- WIP
1. Prepare missiles (copilot seat):
  1. Lasing button cover ... OPEN (copilot weapon grip)
  2. Missile Launch button cover ... OPEN (copilot weapon grip)
  3. Test On/Off key ... JOUR (day) or NUIT (night) as needed (instrument panel under TV and VCB)
  4. HOT missile station selector knob ... as needed (Gray Reset Hat left/right to select station) (instrument panel under TV and VCB)
2. Max range is 4300 m.
  1. If using Viviane TV/IR sighting system: Lase target (TDC press) to establish range.
  2. If using optical periscope, determine range with stadia reticles.
3. Target is locked if white rectangle appears in lower right quadrant of TV crosshairs.
4. Come to a hover and trim.
5. Must be within 3 degrees of centerline to fire missile. Green light shows in Viviane/periscope when in parameters.
6. Press Red Button to fire.