1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A/G - Guns, Cannon, Rockets, Minigun

Master Arm ... ON (B2 button, or switch on instrument panel under radar altimeter)
TV system ... ON

SA342L -- Guns/Cannon
1. Gunsight glass ... Down (click to deploy)
2. Armament Panel Power switch ... M (ON) (center console forward)
3. Pylon Master Arm switch for applicable pylon ... ARM (red guarded switch, center console)
  - If using cannon and rockets and both are armed, only cannon will fire.
Press Trigger to fire.

SA342L -- SNEB rockets
1. Gunsight glass ... Down (click to deploy)
2. Armament Panel Power switch ... M (ON) (center console forward)
3. Pylon Master Arm switch for applicable pylon ... ARM (red guarded switch, center console)
  - If using cannon and rockets and both are armed, only cannon will fire.
1. Ripple/Single switch ... As desired (center console)
2. Press Trigger to fire.

SA342Minigun -- 7.62 mm Minigun
1. Minigun can only be fired by player.
2. Press 3 to go to gunner seat.
3. Aim with head tracking, fire with trigger.