1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

101 - Controls - Joystick
U=Up, D=Down, F=Forward, B=Backward, L=Left, R=Right, P=Press, S-*=Shift-*, L-*=Long-*

Trigger
- P1: --
- P2: Fire weapon (all weapons)
Flip-down Trigger
- P: Launch permission override toggle on/off (forces Launch Authorized; be careful)
- S-P: Cut of Burst select (toggles gun between burst and continuous, flips a switch on the Weapons Control Panel)
Red Button
- P: Fire weapon (all weapons)
- S-P (3x): Eject
Upper Gray Button
P: Center VR view
Lower Gray Button
P: Change Weapon
Trim Hat
- U/D/L/R: Pitch/Roll Trim
- S-U/S-D/S-L/S-R: -- (no autopilot in the Su-25A)
Dish Hat
- U: A/A missile mode (same as B1 button)
- D: A/G mode (same as B4 button)
- L: Gunsight Reticle Switch (toggles fixed gunsight)
- R: Navigation modes (same as B5 button)
- P: Toggle mirrors
MANVR/PC hat -- Mouse and zoom
Index Finger Hat -- View and Game controls
- F: F6 Weapon view	S-F: Active pause
- B: F2 External view	S-B: Info bar view toggle
- U: F1 Cockpit view	S-U: Rearm/Refuel window
- D: F10 Map view	S-D: Show controls indicator
- P: Toggle show control stick	S-P: Toggle show pilot body
Gray Reset Hat -- Weapon selection
- F: Toggle Salvo mode (for rockets, toggles firing one pair of pods at a time or all pods simultaneously; for A2A missiles, toggles firing two missiles about 1.5 seconds apart)
- B: Toggle cannon (and gunpods) on/off
- L: Ripple Interval Decrease (knob on right of Weapon Control Panel)
- R: Ripple Interval Increase (knob on right of Weapon Control Panel)
- P: Ripple Quantity cycle (knob on left of Weapon Control Panel)
Brake lever
P: Wheel brakes (no axis for this plane)