1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201 - Ground - Preflight, Performance Limits

Gyro alignment -- IMPORTANT
- After turning on electrical power, allow the gyros to align for at least 2m30s before moving/taxiing (rearming and starting engines is OK). If you don't allow the gyros to align, the HSI may show an incorrect heading after maneuvering.
- Press Front Thumb Button to toggle stopwatch (second hand and bottom dial of main cockpit clock).

To Rearm and Refuel, you must have engines off and canopy open
1. Shift-Bottom Thumb Button press to turn off engines.
2. T7 up to toggle canopy.
3. When done, Bottom Thumb Button press to start engines.
  - Throttle must be all the way back and electrical power must be on (T1 switch).

Before takeoff
1. Canopy ... Closed
2. Air brakes ... Closed
3. RWR settings and volume ... As needed

Performance limits
- Full internal fuel: 2,835 kg (6,250 lbs)
  - External fuel tank: 620 kg (1,367 lbs) each
  - With 2x external fuel tanks: 4,075 kg (8,984 lbs)
  - With 4x external fuel tanks: 5,315 kg (11,718 lbs)
- Fuel flow varies depending on speed and throttle setting. At 100% throttle at low altitude, endurance may be as low as ~15 minutes. At 95% throttle, fuel burn is approx 2/3rds that at mil power.
- Landing gear and flaps: 400 kph