1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A/G - Stores List

Guided weapons
Name	Weight	Warhead weight	Min range	Max range	Notes
Kh-25ML (AS-10 Karen)	793 lbs	89.6 kg (198 lbs)	1.25 km	7 km
Kh-29L (AS-14 Kedge)	1647 lbs	317 kg (699 lbs)	1.5 km	10 km
S-25L	1102 lbs	150 kg (331 lbs)	0.5 km	2.0 km	340 mm rocket

Bombs
Name	Weight	Bomb type	Warhead type
BetAB-500	948 lbs	Low drag (no parachute or rocket)	Concrete piercing
BetAB-500ShP	935 lbs	High drag (parachute and rocket)	Concrete piercing
FAB-100	220 lbs	Low drag	GP
FAB-250	551 lbs	Low drag	GP
FAB-250-M62	500 lbs	Low drag	GP
FAB-500 M-62	1116 lbs	Low drag	GP
KMGU-2 - 96 x AO-2.5RT	1715 lbs	Dispenser	HE/Frag
KMGU-2 - 96 x PTAB-2.5KO	1490 lbs	Dispenser	HEAT/AP
MDB-2-67U with 4 x FAB-100	1025 lbs	Dispenser/Low drag	GP
RBK-250 - 42 x PTAB-2.5M	540 lbs	Cluster	HEAT/AP
RBK-250-275 - 150 x AO-1SCh	540 lbs	Cluster	HE/Frag
RBK-500 - 268 x PTAB-1M	941 lbs	Cluster	Light HEAT/AP
RBK-500 - 30 x PTAB-10-5	558 lbs	Cluster	Heavy HEAT/AP
RBK-500U - 126 x OAB-2.5RT	941 lbs	Cluster	HE/Frag
SAB-100	220 lbs	Illumination	Illumination

Rockets
Name	Diameter	Weight / per pod	Rounds / per pod	Warhead / type	Min / range	Max / range	Firing / type	Notes
S-13-OF	122 mm	1125 lbs	5	Blast/Frag	1.1 km	3.5+ km	Ripple	Long narrow pods
S-8KOM	80 mm	800 lbs	20	HEAT/AP	0.6 km	3.0 km	Ripple	Pointy pods
S-8OFP2	80 mm	1039 lbs	20	HE/Frag/AP	0.6 km	3.0 km	Ripple	Pointy pods
S-8TsM *	80 mm	791 lbs	20	Smoke (yellow)	0.6 km	3.0 km	Single	Pointy pods
S-24B	240 mm	651 lbs	1	123 kg HE/Frag / (low smoke)	2.0 km	3.0 km	Single	No tube, fires off rail
S-25-O	420 mm	981 lbs	1	150 kg Frag	1.6 km	3.0 km	Single	Bulbous warhead
S-25-OFM	340 mm	1092 lbs	1	190 kg Penetrator	2.0 km	3.0 km	Single	Conical orange "crayon" warhead
S-5KO	57 mm	606 lbs	32	HEAT/Frag	0.6 km	2.5 km	Ripple	Old pods

* = Often banned/not available on servers due to lag issues

Pods
Name	Weight	Type	Notes
SPPU-22-1 Gun Pod	639 lbs	2 x 23 mm gun pod	Stations 4, 5, 6, 7 only (inner two A/G stations)
SPS-141	331 lbs	ECM jamming pod	Station 8 only