1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Preflight, Takeoff, Landing, RWR, Fuel

Takeoff
1. Flaps ... Half or Full.
2. Begin takeoff run.
3. Rotate at 280 kph for Half flaps, or 260 kph for Full flaps.
4. Put pitot tubes at the horizon for a good takeoff angle, about 13 degrees.
5. Raise gear immediately but build up speed before raising flaps. Raise flaps under 400 kph.

Landing
1. Under 400 kph, put down gear and flaps.
2. Pattern speed ~300 kph, final approach speed ~260 kph.
3. Landing speed ~220 to 240 kph.
4. Put pitot tubes at the horizon for a good landing angle, about 13 degrees.
5. Use drag chute if needed (Shift-T5 down). WARNING Don't press the button again until you want to drop the chute.

RWR
- Light in outer ring of large circles indicates primary threat direction.
- Lights in small dots just inside those indicates secondary threats.
- Ring of dashed lines on the inside indicates range/signal strength of primary threat, weakest is all the way to the right, and getting stronger to the left. Ownship marker is the triangle at the left.
- Lights in bottom row of dashes and letters is primary (dashes) and secondary (letters) threat:
  - П	З	X	H	F	C
  - AI radar	LR radar	MR radar	SR radar	EW radar	AWACS
- B and H lights in the center of the plane show relative elevation of primary threat. If both are lit, threat is co-altitude.
- Red flashing circle in the center around the plane is radar lock warning.
- Press Shift-E1 press to toggle RWR to filter out acquisition radars.

Fuel indicator lights
Light	Meaning
I	Empty or no tanks on outer pylons
II	Empty or no tanks on inner pylons
KP	Empty internal wing tanks
3/4	Empty internal 3rd and 4th tanks
Ц	Empty internal central tank
0.5	Less than 500 kg fuel remaining