1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

501 - A/G - Stores List

Pods
Name	Weight	Notes	Stations
L-081 Phantasmagoria ELINT pod	661 lbs	Required to use ARMs	6
Mercury LLTV pod	507 lbs	Provides night vision to Shkval (toggle with Pinky Hat press)	6
MPS 410	331 lbs each, 661 lbs pair	ECM jammer	1/11
SPPU-22-1 Gun Pod	639 lb	2 x 23 mm gun pod	4/5/6/7

Guided weapons -- WIP ranges need testing
Name	Type	Weight	Warhead	Range		Stations
				Min	Max *
Kh-29L (AS-14 Kedge)	SALH	1865 lbs	317 kg (699 lbs)	8 km??	10 km??	5/7
Kh-29T (AS-14 Kedge)	TV/EO	1931 lbs	317 kg (699 lbs)	8 km??	10 km??	5/7
Kh-58U (AS-11 Kilter)	ARM	1843 lbs	149 kg	??	36-120 km	5/7
Kh-25ML (AS-10 Karen)	SALH	794 lbs	90 kg	2 km??	10 km??	3/4/8/9
Kh-25MP ** (AS-10 Karen)	ARM	783 lbs	??	??	??	3/4/8/9
Kh-25MPU ** (AS-10 Karen)	ARM	816 lbs	??	??	??	3/4/8/9
9A1472 Vikhr (AT-16 Scallion)	Beam riding	1179 lbs	8-12 kg	??	??	4/8
S-25L	SALH	1102 lbs	150 kg (331 lbs)	??	??	2/3/4/5/7/8/9/10

* = Max range depends on launch speed and altitude
** = Not sure if any significant difference between these in game

Bombs
Name	Weight	Bomb type	Warhead type	Notes
BetAB-500	948 lbs	Low drag	Concrete piercing
BetAB-500ShP	935 lbs	High drag	Concrete piercing
FAB-100	220 lbs	Low drag	GP
FAB-250	551 lbs	Low drag	GP
FAB-250-M62	500 lbs	Low drag	GP
FAB-500 M-62	1116 lbs	Low drag	GP
KAB-500kr	1235 lbs	TV/EO guided	GP??	stations 5/7 only
KMGU-2 - 96 x AO-2.5RT	1715 lbs	Dispenser	HE/Frag
KMGU-2 - 96 x PTAB-2.5KO	1490 lbs	Dispenser	HEAT/AP
MDB-2-67U with 4 x FAB-100	1025 lbs	Dispenser/Low drag	GP
RBK-250 - 42 x PTAB-2.5M	540 lbs	Cluster	HEAT/AP
RBK-250-275 - 150 x AO-1SCh	540 lbs	Cluster	HE/Frag
RBK-500 - 268 x PTAB-1M	941 lbs	Cluster	Light HEAT/AP
RBK-500 - 30 x PTAB-10-5	558 lbs	Cluster	Heavy HEAT/AP
RBK-500U - 126 x OAB-2.5RT	941 lbs	Cluster	HE/Frag
SAB-100	220 lbs	Illumination	Illumination

Rockets -- WIP range and firing type needs verification
Name	Diameter	Weight / per pod	Rounds / per pod	Warhead / type	Min / range	Max / range	Firing / type	Notes
S-13-OF	122 mm	1124 lbs	5	Blast/Frag	1.1 km	3.5+ km	Ripple	Long narrow pods
S-8KOM	80 mm	800 lbs	20	HEAT/Frag	0.6 km	3.0 km	Ripple	Pointy pods
S-8OFP2	80 mm	1063 lbs	20	MPP	0.6 km	3.0 km	Ripple	Pointy pods
S-8OM	80 mm	836 lbs	20	Illumination	??	??	??	Pointy pods
S-8TsM *	80 mm	791 lbs	20	Smoke (orange)	0.6 km	3.0 km	Single	Pointy pods
S-24B	240 mm	650 lbs	1	123 kg HE/Frag / (low smoke)	2.0 km	3.0 km	Single	No tube, fires off rail
S-25-O	420 mm	981 lbs	1	150 kg Frag	1.6 km	3.0 km	Single	Bulbous warhead
S-25-OFM	340 mm	1091 lbs	1	190 kg Penetrator	2.0 km	3.0 km	Single	Conical orange "crayon" warhead
S-5KO	57 mm	606 lbs	32	HEAT/Frag	0.6 km	2.5 km	Ripple	Old pods

* = often banned/not available on servers due to lag issues