1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A/G - General setup, Shkval use, Guided weapons

A/G Master Mode ... B4 press

All
- Press Lower Gray Button to cycle weapons
- Selected weapon is shown on the HUD in English, and in the armament panel with lights and letters:
  - Б = bombs
  - УР = missiles
  - НРС = rockets
  - ВПУ = gun, remaining rounds shown in the lower right of the panel: К = full, then 1/2, 1/4
  - Remaining gun rounds are also in the bottom right corner of HUD when in gun mode, shown in quarters (4, 3, 2, 1).
- Countermeasures ... As needed (Top Hat -- F: chaff, B: flares, U: ECM (if carrying pods), D: IRCM)
- Weapons of the same type fire from the outside in.

Shkval -- Used for Laser Guided weapons, and to designate targets for TV guided bombs, gunpods, and CCRP bombing
Turn on Shkval TV screen (Pinky Switch down).
  - HUD will show TV on upper left when Shkval is active.
  - If using Mercury LLTV pod, press Pinky Hat press to toggle LTV mode.
1. Use TDC slew to slew crosshairs onto target in Shkval.
2. Controls:
  1. Lock target/ground lock ... TDC press
  2. Unlock target ... shift TDC press
  3. Re-center on HUD ... Middle Finger Hat press
  4. Zoom in/out ... Middle Finger Hat up/down
  5. Tracking gate size ... Middle Finger hat left/right
3. Press TDC press to ground lock. If contrast is high enough, Shkval will automatically lock on the target, but target lock is not required to use weapons.
  - "KC" at top right indicates ground lock, "AC" at top right indicates target contrast lock
  - Number at top left is size of targeting box in meters
  - "LR" at bottom with number indicates laser ranging active, range in km
1. When starting attack run, turn on laser (Pinky Button press).
2. Range scale will be shown on left side of HUD.
3. When off the attack run, turn off laser (Pinky Button press). Laser will overheat if left on for more than about a minute.

Guided weapons (Laser guided: Kh-25ML, Kh-29L, S-25L, 9A1472 Vikhr; TV guided: KAB-500kr)
Laser guided weapons (except Vikhr??) use laser code 1113 and can be buddy-lased from other platforms.
Lock target with Shkval (see steps above)
  - Ground lock ("KC") is ok, target contrast lock ("AC") is not required to use weapons.
1. When starting attack run, turn on laser (Pinky Button press).
2. Range scale will be shown on left side of HUD.
3. When in range and you have LA on bottom of HUD (Launch Authorized), press and hold Trigger to fire.
  - If using Vikhrs, remain pointing at target since it's a beam-rider.
Turn off laser (Pinky Button press).

ARMs (Kh-25MP, Kh-25MPU, Kh-58U), L-801 ELINT pod is required
Turn on ELINT pod (Pinky Hat up).
  - HUD will show ETS at bottom left when pod is active, and positions of detected emitters will be shown on HUD.
1. Use TDC to slew square designator on HUD over the desired emitter marker, press TDC press to lock.
2. When in range, fire with Trigger.
- If Shkval TV screen is also on (Pinky Hat down), it will automatically be slaved to emitter location when emitter is locked.
- When ELINT pod is active, only ARMs can be selected, but if Shkval is slaved to emitter you can turn off the ELINT pod and select other weapons.