1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

503 - A/G - Cannon, Bombs, Rockets

All
- Press B4 to set A/G Master Mode
- Press Lower Gray Button to cycle weapons

Cannon
1. Press Gray Reset Hat back to toggle cannon on.
2. Press Trigger to fire. Fires in short bursts.

Unguided bombs
All
1. Launch permission override ... Off (not sure exactly how to tell, but "LA" should not be on the HUD until release parameters are met)
2. Set ripple and interval. Weapons Control Panel is in the bottom left corner of instrument panel.
  - Press Gray Reset Hat left/right to turn interval knob (left side of Weapons Control Panel):
    - ЗАЛП -- Salvo, release all weapons simultaneously
    - 0.1 - 0.2 - 0.3 - 0.4 -- Release in intervals of this many seconds
    - СЕРИЯ КМГУ-МБД -- Special setting for KMGU submunitions dispenser and MDB-2-67U MER, opens KMGU sequentially at 2-second intervals, and drops MER bombs at 0.3-second intervals.
  - Press Gray Reset Hat press to turn quantity knob (right side of Weapons Control Panel):
    - ПО 1 -- Single (may only work for inner 4 pylons for some weapons, outer pylons may drop in pairs to maintain balance)
    - ПО 2 -- Pairs
    - ПО 4 -- Fours
    - ВСЕ -- All
CCIP bombing (with automatic CCRP mode) -- No target designated
Put the pipper on the target and hold Trigger until bomb drops.
  - If there's no vertical bomb fall line, holding Trigger will enter CCRP mode. Diamond indicator will appear over target point, bombs will drop when range scale arrow on left of HUD reaches bottom.
CCRP bombing -- With Shkval target designated
Lock target with Shkval (see steps on other checklist)
  - Ground lock ("KC") is ok, target contrast lock ("AC") is not required to use weapons.
1. When starting attack run, turn on laser (Pinky Button press).
2. Range scale will be shown on left side of HUD.
3. When in range, hold Trigger to enable the CCRP path pipper. This should appear just above your flight path marker on the HUD. Fly so the vertical tail of the flight path marker aligns exactly with the pipper.
4. Bomb will drop when range scale reaches bottom.
5. Turn off laser (Pinky Button press).

Gunpods
1. Press Gray Reset Hat back to toggle cannon on.
2. Set gunpods aiming mode. Weapons Control Panel is in the bottom left corner of instrument panel.
  - Press Gray Reset Hat press to turn quantity knob (right side of Weapons Control Panel), also automatically sets the interval knob as noted:
Quantity knob (you change this)	Interval knob (changes automatically)
	No target	With target and laser on
ПО 1 -- Internal gun only ("GUN") / ВСЕ -- All gunpods ("ALL")	0 -- Fixed boresighted	0 -- Fixed boresighted
ПО 2 -- Single pair of gunpods ("GNPD") / ПО 4 -- All gunpods ("GNPD")	ФИКС -- Depressed to fixed angle (use Middle Finger Hat left/right to adjust angle up/down)	ПРОГР -- Automatic tracking

Press Trigger to fire.

Rockets
Put pipper on the target, hold Trigger to ripple fire.
  - Rockets fire very quickly, about 1.3 seconds per pod for S-8s, use short bursts.

KMGU submunition dispensers
- Level attack, 50-150 m.
- Each dispenser covers about 0.23 nmi (425 m), so two dispensers in special sequence timing (СЕРИЯ КМГУ-МБД) will cover about 0.46 nmi (850 m)