1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

103 - Controls - Throttle Base
U=Up, D=Down, F=Forward, B=Backward, L=Left, R=Right, P=Press, S-*=Shift-*, L-*=Long-*

Mode selector
Turn: --
Flaps lever
Axis: --
T1 switch
F: Toggle Electric Power
T2 switch
F: Jettison weapons (must be pressed repeatedly to drop all weapons, order is outer to inner pylons, drop tanks first, then A2G weapons, then A2A weapons; pods are not jettisoned)
T3 switch
F: Reset Master Caution audio warning
T4 switch
F: --
Lighted Buttons -- Master Modes
B1: Longitudinal missile mode	B2: BVR Master Mode	B3: Next Waypoint/Airfield
B4: A/G Master Mode	B5: Cycle Nav Mode:	B6: Previous Waypoint/Airfield	No Task, Route, Return, Landing
T5 switch -- Landing Gear
- U/D: Landing Gear up/down
- S-D: Deploy drag chute, drop chute after use
T6 switch -- Flaps
- U: Flaps up
- D: Flaps up/down (toggles between flaps up and takeoff position)
- S-U: Refueling Probe toggle (takes about 3 minutes to retract to simulate depressurize/purge cycle) (Su-33 only)
- S-D: Flaps Landing Position (full down)
T7 switch -- Canopy
- U: Canopy up/down toggle
- S-U: Wing fold toggle (Su-33 only)
- S-D: Tail hook toggle (Su-33 only)
E1 dial -- Kneeboard and RWR
- P: Kneeboard toggle
- L/R: Flip pages
- S-P: RWR mode cycle
- S-L/S-R: RWR volume up/down
E2 dial -- (no NVGs)
- P: --
- L/R: --