1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

201 - Ground - Preflight, Takeoff, Landing, RWR, Performance Limits

To Rearm and Refuel, you must have engines off and canopy open
1. Shift-Bottom Thumb Button press to turn off engines.
2. T7 up to toggle canopy.
3. When done, Bottom Thumb Button press to start engines. Make sure electrical power is on (T1 switch) and throttle is at idle.

Before takeoff
1. Canopy ... Closed
2. Air brakes ... Closed
3. RWR settings and volume ... As needed

Performance limits
- Fuel: 9400 kg/20723 lbs internal
  - Su-27 cannot carry droptanks
- Landing gear and flaps: 400 kph??