1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

301 - Flight - Takeoff, Landing, RWR, Navigation, Autopilot

Takeoff
1. Flaps ... Up.
2. Begin takeoff run.
3. Rotate at 270 kph.

Landing
1. Under 400 kph, put down gear and flaps.
2. Landing speed ~220 to 240 kph.??
3. Keep vertical speed low, landing gear is weak.
4. Use drag chute if needed (Shift-T5 down). WARNING Don't press the button again until you want to drop the chute.

RWR
- Light in outer ring of large circles indicates primary threat direction.
- Lights in small dots just inside those indicates secondary threats.
- Ring of dashed lines on the inside indicates range/signal strength of primary threat, weakest is all the way to the right, and getting stronger to the left. Ownship marker is the triangle at the left.
- Lights in bottom row of dashes and letters is primary (dashes) and secondary (letters) threat:
  - П	З	X	H	F	C
  - AI radar	LR radar	MR radar	SR radar	EW radar	AWACS
- B and H lights in the center of the plane show relative elevation of primary threat. If both are lit, threat is co-altitude.
- Red flashing circle in the center around the plane is radar lock warning.
- Press Shift-E1 press to toggle RWR to filter out acquisition radars.

Navigation
- Press B5 to cycle NAV Master Modes: No Task, En Route, Return, and Landing.
- Nav mode is indicated in bottom left of HUD, and distance is shown in bottom center. Modes:
  - No Task -- Nothing in the HUD.
  - En Route -- "ENR" in HUD. Navigates to regular pre-planned waypoints.
  - Return -- "RTN" in HUD. Navigates to the runway approach point for the selected airport ID (see list on next page).
  - Landing -- "LNDG" in HUD. Navigates to the end of the actual runway for the selected airport ID (see list on next page).
  - Current waypoint can be seen in the MFD in certain modes (A2G mode and NAV modes other than No Task).
- HSI indicator also shows navigation information:
  - Distance to the next waypoint in top left corner.
  - Green needle with a diamond is the direct bearing to the waypoint.
  - Double-line white arrow is the course deviation indicator. The CDI shows a bearing to get back onto the line between the previous and current waypoints, and is what the autopilot Route Following mode will follow.

Autopilot -- WIP/TODO
- Press shift-Trim Hat down for level autopilot.
- Press shift-Trim Hat up or shift-Trigger 2nd Stage to disengage AP.
- You can also disengage by moving the stick more than a certain amount, but that may mess up your trim.
- Hold shift-Trigger 1st Stage to temporarily override autopilot. When released, autopilot will be reset to current altitude and heading.