1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

401 - A/A - Radar and EO use

BVR combat and Radar/EO use
1. Press B2 to enter BVR Master Mode.
2. Press Pinky Switch up to turn on radar, or down to turn on EO.
  - Top left of HUD shows RL when radar is on, EO when EO is on, or EORL when both are on.
Radar:
1. When Radar is on, HUD shows top-down radar display (left/right is azimuth and up/down is range).
2. In the HUD, enemy contacts are a single line of dots, friendly contacts are a double line of dots. The number of dots shows the RCS of the contact:
  - 1 dot: <= 2 m2
  - 2 dots: 2 m2 to 30 m2
  - 3 dots: 30 m to 60 m2
  - 4 dots: > 60 m2
1. In the MFD, all contacts are shown as a "T". Enemy contacts have a "V" or nothing at the base of the T, friendly contacts have a "O" at the base of the T. Contact speed is the length of the leg of the T (longer = faster), altitude is the width of the top of the T (longer = higher).
2. When a target is locked:
  - Bottom left of HUD shows IFF: "A" for enemy, "AFR" for friendly.
  - Bottom left of HUD shows arrow giving relative target aspect. If arrow is pointing down, target is coming toward you; if arrow is pointing up, target is going away from you.
Radar elevation and azimuth:
  - Left/right scan can be set with Middle Finger Hat left/right. Left/right scan is shown with horizontal line at bottom of HUD.
  - Elevation is set indirectly. First set the target's range with Middle Finger Hat shift-up/down. Range is shown at bottom center of HUD. Then set target's relative altitude in thousands of meters with Middle Finger Hat up/down. Elevation is shown on right side of HUD, along with two marks showing your HUD FOV.
Vertical lines of repeating contacts are jamming you.
  - You can lock a jamming spike and fire an R-27 in HOJ mode. Range will be unknown, so fire only when you think you're close enough.
1. Change radar range with Top Hat Ring forward/back. Display range is shown in upper left of HUD at the top of the range bar: 5, 10, 25, 50, 100, 200, 500 km
2. TWS Mode
  1. Cycle TWS mode with Middle Finger Hat press.
  2. To "bug" a target, just move the designator over the target, it will automatically lock if it's closer than 85% of the current selected weapon's absolute max range (longer than RMAX).
  3. When target is just about to reach RMAX, radar will automatically enter STT mode on the target.
    - You can also force a STT lock manually with TDC press.
  - (NOTE There is no TWS2 mode in the Su-27s)
1. PRF
  1. PRF is shown in the top left of the HUD, either ILV (interleaved), HI, or MED.
  2. Change PRF with Middle Finger Hat shift-press.
  3. Use MED for targets going away from you or at closer range (<45 km).
  4. Use HI for targets coming toward you or at longer range (>45 km).
  5. ILV has 25% less range.
EO:
1. When EO is on, HUD shows longitudinal/boresight EO display (left/right is azimuth and up/down is elevation).
2. WARNING EO system does not do IFF, all contacts look the same so verify your target.
3. In the HUD, all contacts are a single line of dots. The number of dots is the relative IR strength of the contact. More dots = closer or hotter/rear aspect, less dots = farther or cooler/front aspect
4. If you fire a radar missile on an EO target, the radar will turn on automatically.
5. You can IFF your EO target by flashing your radar (Pinky Switch up) when the EO target is locked. If the bottom left of the HUD shows AFR when the radar is on, the target is friendly. If it stays showing A, the target is enemy.

WVR combat and CAC (dogfight) modes
Use Dish Hat for CAC (dogfight) modes:
  - U: Boresight scan
  - D: Vertical scan
  - P: HMD sight
1. When using any CAC (dogfight) mode, you must press TDC press to lock.
2. Press Trigger to fire.