1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A/G - Cannon, Bombs, Rockets

All
Press B4 to set A/G Master Mode
- Press Lower Gray Hat to cycle weapons
- Selected weapon is shown on the HUD in English, and in the armament panel with lights and letters:
  - Б = bombs
  - УР = missiles
  - НРС = rockets
  - ВПУ = gun, remaining rounds shown in the lower right of the panel: К = full, then 1/2, 1/4
  - Remaining gun rounds are also in the bottom right corner of HUD when in gun mode, shown in quarters (4, 3, 2, 1).
- Countermeasures ... As needed (Top Hat -- F: chaff, B: flares, U: ECM (if carrying pods))
- Weapons of the same type fire from the outside in.

Cannon
1. Press Gray Reset Hat backward to toggle cannon on.
2. Press Trigger to fire. Fires in short bursts.

Unguided bombs
All
1. Launch permission override ... Off (not sure exactly how to tell, but "LA" should not be on the HUD until release parameters are met) (Red Button press)
2. Set Salvo mode with Gray Reset Hat shift-press. Default is off. HUD shows a number above weapon pylon dashes for pylons that will be released. If in doubt, force Launch Permission Override (Red Button press) to see pylon release numbers, then turn the override back off.
3. There is no ripple or interval setting.
CCIP bombing (with automatic CCRP mode)
Put the pipper on the target and hold Trigger until bomb drops.
  - If there's no vertical bomb fall line, holding Trigger will enter CCRP mode. Diamond indicator will appear over target point, bombs will drop when range scale arrow on left of HUD reaches bottom.

Rockets
Put pipper on the target, hold Trigger to ripple fire.
  - Rockets fire very quickly, about 1.3 seconds per pod for S-8s, use short bursts.

KMGU submunition dispensers
- Level attack, 50-150 m.
- Each dispenser covers about 0.23 nmi (425 m).