1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

103 - Controls - Throttle Base
U=Up, D=Down, F=Forward, B=Backward, L=Left, R=Right, P=Press, S-*=Shift-*, L-*=Long-*

Mode selector
Turn: Selective Jettison selector sleeve, position 2 is SAFE (T2 switch is jettison button)
Flaps lever
Axis: --
T1 switch
F: Holds FCS BIT switch when forward (right wall of cockpit, used when doing some startup checks)
T2 switch
F: Selective Jettison button press and hold when forward (use with Mode selector)
T3 switch
F: FLIR switch (targeting pod) ON when forward, STBY when back
T4 switch
F: LTD/R switch (laser designator) ARM when forward, SAFE when back
Lighted Buttons -- Master Modes, Master Arm, carrier calls
B1: Toggle A/A mode	B2: Master Arm ON	B3: Salute
- B4: Toggle A/G mode	B5: Master Arm OFF	B6: Hornet Ball
- S-B6: Catapult Hook-up (for non-Super Carrier)
T5 switch -- Landing Gear and Hook
- U/D: Landing Gear up/down
- S-U/S-D: Hook up/down
T6 switch -- Flaps and Refueling Probe
- U/D: Flaps switch up/down one notch
- S-U/S-D: Refueling probe extend/retract
T7 switch -- Canopy
U/D: Canopy up/down
E1 dial -- Kneeboard
- P: Kneeboard toggle
- L/R: Flip pages
S-Rotate: RWR volume up/down
E2 dial -- NVGs
- P: Toggle NVGs on/off
- L/R: NVG gain up/down
- S-P: Toggle helmet visor