1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

102 - Controls - Throttle Grip
U=Up, D=Down, F=Forward, B=Backward, L=Left, R=Right, P=Press, S-*=Shift-*, L-*=Long-*

Top Hat -- "Countermeasures Switch (CMS)" (NOTE The manual and Chuck's are wrong; these are the correct controls for the CMS Switch, now the same as the A-10C-II.)
- F: 6 Chaff (CMS right)
- B: 6 Flares (CMS left)
- U: 1 Flare (CMS fwd)	L-U: Next program
- D: 1 Chaff (CMS aft)	L-D: Previous program
- P: Toggle selected program	L-P: Toggle ECM
- (In real plane, CMS aft=1 chaff, CMS fwd=1 flare, CMS left=6 flare, CMS right=6 chaff)
Top Hat Ring
- F: CMSP NXT rocker up (next CM program or increase value)
- B: CMSP NXT rocker down (previous CM program or decrease value)
Middle Hat -- "Mic Switch"
- U: (SRS radio 1 PTT)
- D: (SRS radio 2 PTT)
- S-U: Radio 1 PTT (opens comms menu for radio 1)
- S-D: Radio 2 PTT (opens comms menu for radio 2)
Bottom Hat -- "Speed Brake Switch"
- F: Extend speedbrakes (keeps extending while held, stays open when you let go)
- B: Retract speedbrakes (keeps retracting while held)
Front Thumb Button/Rear Thumb Button -- "China Hat"
SOI->	TAD	TGP	HUD	AIM-9	Mav
Fwd	FOV EXP cycle	FOV toggle	Set MAV as SOI	Uncage	FOV toggle
Fwd-Long	Slave all to SPI			Slave AIM-9 to TGP	Slave all to SPI
Back	Reset cursor	Set TGP to boresight	Cage TDC to VV	Cage, then Missile step
Back-Long	Slave TGP (only) to steerpoint

Bottom Thumb Button
- P: Right throttle to idle detent (used for engine start)
- S-P: Left throttle to idle detent (used for engine start)
Ministick -- Slew Control
Axes: Slew
P: --
Middle Finger Hat -- "DMS (Data Management Switch)" (forward on real switch is up)
SOI->	TAD	TGP	HUD	AIM-9	Mav
Up (fwd)	TAD zoom in	Zoom in	Next Steerpoint	--	Slew
Down (aft)	TAD zoom out	Zoom out	Prev Steerpoint	--	Slew
Left	--	FLIR auto focus	Gunsight/DSMS profile cycle	A-A target toggle	Slew
Left-Long	Toggle broadcasting SPI (TAD MFD shows SPI ON/OFF)
Right	Toggle Centered/Decentered	Laser mode cycle LSR->IR->BTH	Gunsight/DSMS profile cycle	A-A target toggle	Slew
Right-Long	--	LSS toggle	--	--	--

Ring Finger Slider
U/D: --
Pinky Switch -- "Boat Switch" (forward on real switch is up)
SOI->	TAD	TGP	HUD	AIM-9	Mav
Up (fwd)	--	FLIR BHOT	--	--	Black symbols
Press	--	CCD	--	--	Force correlate/Auto
Down (aft)	--	FLIR WHOT	--	--	White symbols

Pinky Button -- "Left Throttle Button"
P: Toggle autopilot
Pinky Wheel -- "Pinky Switch"
- F: Default external lights
- P: Exterior lights off
- B: Lights according to panel