1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

304 - Flight - Countermeasures

Countermeasures -- WIP needs verification
- Countermeasures Hat controls:
  - F: 6 Chaff
  - B: 6 Flares
  - U: 1 Flare	L-U: Next program
  - D: 1 Chaff	L-D: Previous program
  - P: Toggle selected program	L-P: Toggle ECM
- Current CM program is shown on the display under the HUD, the letter A-M on the left under CHAFF.
- Current CM mode (STBY, MAN, SEMI, AUTO) is shown with the letter under FLARE.
- Change CM program with CM Hat up long or CM Hat down long, or faster by using the NXT rocker switch on the CM panel (left console inboard forward).
- When you change programs, the CMSP panel will briefly show the settings for the selected program.
- ECM jammer mode is shown on the front panel as AIR, SAM1, SAM2, or AAA. Change with the arrow button next to it.
  - AIR - air-to-air radars
  - SAM1 - single-digit SAMs: SA-2, SA-3, SA-5??, SA-6, SA-8
  - SAM2 - double-digit SAMs: SA-10, SA-11, SA-15, 2S6 (SA-19)
  - AAA - gun systems: ZSU-23-4, Gepard??, M-163 Vulcan??
Default programs:
Prog	Ch	Fl	Int	Cycle
A	2	0	1	10
B	4	0	0.5	10
C	0	4	1	10
D	2	2	1	10
E	2	2	0.5	10
F	4	4	1	10
G	4	4	0.5	10
H	1	0	1	1
I	2	0	1	1
J	0	1	1	1
K	0	2	1	1
L	1	0	1	20
M	0	1	1	20

Change program settings: -- WIP but should be basically accurate
Select a program with CMSP panel (right console inboard forward) NXT rocker switch (Top Hat Ring forward/back) or CM Hat forward long/back long.
  - Selected program is shown in CMSC (under HUD) as the letter under CHAFF.
1. On the CMSP panel (right console inboard forward), set the DISP switch to MENU (forward) to display the current program settings.
2. Press the ^ arrow button below any setting to change it, then use the NXT rocker switch (Top Hat Ring forward/back) to increase/decrease the value.
3. Press RTN button to save.