1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

306 - Flight - TAD page, SADL

TAD page (Tactical Awareness Display) -- WIP
- Control "+" cursor with TDC ministick.
- Elongated diamond "◊" shows where TPOD is pointing.
- Controls, with TAD page as SOI:
  - DMS up/down ... Zoom in/out
  - DMS right ... Toggle centered/decentered
  - TMS left long ... Toggle broadcasting SPI (R1 OSB shows SPI ON/OFF) (works in all SOI)
    - NOTE In A-10C, this is DMS left long.
  - Forward Thumb Button short ... Cycle "EXP" zoom in on cursor location
    - Sets map to North Up while in EXP mode.
    - Regular Zoom controls remain active, and moving TDC ministick slews the whole map view.
  - TMS forward ... Hook symbol under cursor
  - TMS back ... Unhook
  - TMS forward long ... Set hooked symbol as SPI
  - TMS right ... Drop markpoint at cursor (you can then hook it and set it as SPI, or see below)
  - TMS right long ... Set last markpoint as SPI
- OSBs:
  - T1 ... Go to options page.
  - T2-T5 ... Set preconfigured display settings.
  - L1 ... Cycles map modes. AUTO=Map changes based on zoom level. MAN=Current map type is used for all zoom levels (allows zooming out further and still show map). OFF=Map off
  - L3 ... Cycles relative bearing/distance shown in bottom right.
    - E.g. OWN/HOOK shows the bearing/distance FROM you TO the hook, while HOOK/OWN shows the bearing/distance FROM the hook TO you.
  - L4 ... Adds the current SPI?? as a waypoint to your current flightplan.
  - R1 ... ??
  - R4 ... Cycles showing Lat/Long or MGRS coords.
  - R5 ... NET page, set up your ownship and group network IDs, and send messages.
- Range shown in the upper right is the radius of the outer range ring.

SADL -- TODO