1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

502 - A/G - LGBs

IMPORTANT: Do not set weapons to use laser codes 17xx. The A-10C and A-10C II cannot lase with 17xx, only 1688 or below.

Laser Guided Bombs -- WIP needs verification/organization
1. Set up for CCRP bombing as described on other page.
2. Designate a target with the TGP (see other page) and set as SPI with TMS forward long (Gray Reset Hat forward long).
  - Setting as SPI is necessary to designate the target for the CCRP calculations.
1. Drop on target as with CCRP mode.
2. Toggle laser firing with Flip-down Trigger press.

Valid laser codes:
Format is ABCC, A=1, B=1-7, C=1-8, never 0 or 9. Range should be 1111 to 1788. However the A-10C and A-10C II cannot set B=7.