1xx - Controls	2xx - Ground	3xx - Flight	4xx - A2A	5xx - A2G	6xx - Misc

504b - A/G - Force Correlate, AGM-65L Maverick

Fence in (switches on lower left instrument panel):
- MASTER ARM ... ARM
- GUN PAC ... ARM
- LASER ... ARM
- TGP ... ARM

Force-Correlate with AGM-65G/K Mavericks (EO only) -- WIP needs verification
1. Designate SPI with TPOD.
2. Press China Hat forward long (Front Thumb Button forward long) to point all sensors at SPI.
3. Press Boat Switch Center (Pinky Hat press) to enter Force-Correlate mode on Maverick. Maverick sensor will be slaved to a kind of image-lock using the scene as a whole.
4. Launch at up to 11.0 nmi (10.0 recommended).

AGM-65L Mavericks (laser guided) -- TODO
1. Select missile and power on (takes 30 seconds to spin up the gyros).
2. Designate target with TGP and fire the laser (Flip-down Trigger press to toggle).
3. Maverick page should show laser reticle with X showing missile seeker pointing. X turns to solid square when locked on the laser. Range DLZ shown on left of HUD. Fire with Red Button.